## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2020]
Lecture 17
03/02/2020
Dan Negrut, 2020 ME759 UW-Madison

## Slide 2: Quote of the day
“The happiness of your life depends upon the quality of your thoughts.”
-- Marcus Aurelius, Roman Emperor [121 – 180 AD]

## Slide 3: Before we get going…
Last time:
  CUDA streams, wrapping up
  Tools of the trade: GPU debugging & profiling
Today:
  Advanced GPU memory issues
    Zero-copy memory
    Unified Virtual Addressing
    Managed memory
Other tidbits:
  Assignment due on Thursday at 9 pm
  One more “GPU computing” lecture
  Finishing teaching early – trip to Italy cancelled
    Last lecture (the 28th), on April 3
  April 15, at 7:15 PM
Kernel <<< >>>
cudaMemcpyAsync(H2D)
cudaMemcpyAsync(D2H)
K2
HD3
K1
K3
HD1
DH1
DH2
DH3
HD2
HD4 K4 DH4
DH2
K2
K3
K4
cudaMemcpyAsync(H2D)
K1 DH1
DH3
DH4

## Slide 4: Unified Memory (Managed Memory) in CUDA

## Slide 5: Multi-Socket Configurations [four sockets: Intel S4600LT2 Xeon E5-4600 Chipset-C600-A Socket-R LGA-2011 1.46Tb DDR3-1600MHz Server Motherboard]
[credit]
: Memory Bank
: CPU Socket

## Slide 6: The underlying theme of today’s lecture
Helpful to not think of the physical memory as one contiguous thing
Rather, an amalgamation of bits and pieces
Another way to look at it: regard it as a “pool of physical memory”
Why: today the pool of physical memory includes the memory of the GPU[s]

## Slide 7: Finding the needle in the haystack
If the pool includes all the memory of the system, how do you find what you need?
Rely on the translation table & the concept of virtual memory
Use 49 instead of 48 bits to represent addresses in this virtual memory
NOTE: although the OS is 64 bits, modern systems typically use only 48 bits for addresses
  64 bits would index 18,446,744,073,709,551,615 bytes – way more than what we see in reality

## Slide 8: Virtual vs. Physical Memory [old slide]
Virtual memory: dally and quaint fictitious space of 232 addresses (on 32 bit architectures) in which a process sees its data being placed, the instructions stored, etc.
  Correction: you have 49 bits instead of 32
    You can index into 562,949,953,421,311 bytes (about 562 Terabytes) – hundreds of times more than what in use on a system nowadays
Physical memory: a busy [perhaps heterogeneous] place that hosts at the same time data and instructions associated with many applications simultaneously running on the system
Notes: The Virtual Memory paradigm allows:
running programs that require more memory than physically available
running multiple programs “simultaneously” (multi-tasking)
allows handling of memory segmentation
allows transparent and unitary handling of memory and secondary storage (hard disk / solid state disk)
gets away with the need to use relative addresses or program relocation
Hardware component in charge: Memory Management Unit (MMU)

## Slide 9: Virtual Memory: The Page Table [old slide]
Virtual memory allows the processor to work in a virtual world in which a process seems to have exclusive access to a very large memory space
This virtual world is connected back to, or mapped back into, the physical memory through a Page Table
  This is one level of indirection
Notes: Back to the MMU’s job: Translating between virtual addresses and physical addresses. This is done through a so-called Page Table
To see how the PT works, let’s first dissect a virtual memory address…

## Slide 10: The UVA
Key observation: relatively recently, the GPU and CPU decided to share together one virtual memory space
  UVA: Unified Virtual Address
  UVAS: Unified Virtual Address Space
The trick is to translate an address from this 49-bit UVAS into the pool of physical memory
Notes: Back to the MMU’s job: Translating between virtual addresses and physical addresses. This is done through a so-called Page Table
To see how the PT works, let’s first dissect a virtual memory address…

## Slide 11: The Page Table & The Translation Process
A virtual address has two parts (address butchering):
  The page number
  The offset (last 12 bits)
Example below assumes a 32-bit OS with virtual pages of bytes
[physical memory]
process
Pool of Physical Memory (includes GPU memory now)
Notes: The virtual memory is split into pages.
The physical memory is split into frames.
This is for a 32-bit OS with virtual pages of 4096 bytes.
4096 = 2^12  need 12 bits to indicate the offset in the page.
(Note: unit of address resolution is 8 bits  a virtual page holds 4 KB)
The remaining 32-12 = 20 bits used to index into the Page Table to get the corresponding frame number (which is held in N bits)

## Slide 12: Anatomy of a Virtual Memory Address
A page of virtual memory corresponds to a frame of physical memory
The size of a page (or frame, for that matter) is typically 4096 bytes
  Compare to 64 bytes, the size of a cache block (line)
212 = 4096: 12 bits of the address are sufficient to relatively position each byte in a page
  Bits marked 0 through 11 on the previous slide

## Slide 13: The Translation Process
Example: imagine that your physical memory is 2 GB
The physical address has 31 bits: 231=2GB
Then the page table converts the bits 12 through 31 of the virtual address into bits 12 through 30 of the physical address
Notes: N depends on the amount of available RAM:
e.g. for 2GB of RAM, N=19. Because 2GB=2^31 bits and 31=12+19
since N max = 20  a 32-bit OS can reference 4GB of memory  a maximum of 1 million pages
each address requires 4bytes  the PT takes 4MB
each active application has its own PT  lots of memory just for the PTs

## Slide 14: Putting things in perspective, today’s presentation
Premise: Managing and optimizing hostdevice data transfers a bit of a nuisance
Punch line: Unified Memory (UM) support, available as of CUDA 6, simplifies this task
Our goals today:
  Briefly review history of CUDA host/device memory management
  Explain how UM makes CUDA low-level programming more palatable

## Slide 15: Good to keep in mind
In this Unified Memory discussion:
  We are not going to learn anything that we couldn’t live without
  Discussion focus: how GPU programming became more friendly/convenient in relation to data movement
    A matter of improved productivity
Remark: A byproduct of this discussion is a better understanding of how CUDA is evolving
  Happens as we speak…

## Slide 16: Backdrop, cudaMemcpy
cudaMemcpy: A staple of CUDA, available in release 1.0
The drill
  Get some memory space in device memory (cudaMalloc call)
  Data transferred from host memory into device memory with cudaMemcpy
  Data processed on the device by invoking a kernel
  Results transferred from device memory into host memory with cudaMemcpy
  Free the cudaMalloc-ed memory on the device
  Kick back and relax (reach for a strong one?)

## Slide 17: Backdrop, cudaMemcpy
Memory allocated on the host with malloc
Memory allocated on the device using the CUDA runtime function cudaMalloc
Data moved back-and-forth, host to/from device, over the PCI-E pipe

## Slide 18: The PCI-E Pipe, Putting Things in Perspective
PCIe x 16: peak bandwidth (what’s reasonable to expect in parentheses) (per direction data)
  V1: 4.0 (3) GB/s
  V2: 8.0 (6) GB/s
  V3: 15.8 (12) GB/s
  V4: 31.5 (???) GB/s
Bandwidths above relatively small, see for instance (values provided are middle of the road)
  Host memory bus: about 25 – 50 GB/s per socket
  GPU global memory bandwidth: 400 – 900 GB/s
Notes: (now, Haswell is higher?)

## Slide 19: cudaHostAlloc: helps improve host/device transfer speeds
Host/Device data transfer speeds could be improved if host memory was not pageable
Therefore, rather than malloc-ing, allocate host memory using CUDA’s cudaHostAlloc()
Nothing magic, data still moves back-and-forth through same PCI-E pipe albeit at a faster clip

## Slide 20: cudaHostAlloc: A friend, with its pluses and minuses
cudaHostAlloc cons
  cudaHostAlloc-ing large amounts of memory can negatively impact overall system performance
    Why? It reduces the amount of system memory available for paging
    How much is too much? Not clear, dependent on the system and the applications running on the machine
  cudaHostAlloc memory allocation speed is small - ballpark 5 GB/s
    Allocating 5 GB of memory time-wise comparable to moving that much memory over the PCI-E bus

## Slide 21: cudaHostAlloc: A friend, with its pluses and minuses
  Enables faster device host, back-and-forth transfers
  Enables the use of asynchronous memory transfer and kernel execution (topic covered before)
    Draws on the concept of CUDA stream
    “in/out data copy” and “execution” engines working at the same time
  3. Enables mapping of the host pinned memory into the memory space of the device
    Device now capable to access data on host while executing a kernel or other device function

## Slide 22: cudaHostAlloc: Function Prototype
cudaError_t cudaHostAlloc(void** pHst, size_t sz, unsigned int flag);
Last argument (“flag”) controls the magic
“flag” values: cudaHostAllocPortable, cudaHostAllocWriteCombined, etc.
The “flag” of most interest is “cudaHostAllocMapped”
  Maps the memory allocated on the host in the memory space of the device for direct access

## Slide 23: Zero-Copy (Z-C) GPU-CPU Interaction
What’s gained if you pin host memory via cudaHostAlloc?
  The ability to access a piece of data from pinned and mapped host memory by a thread running on the GPU without a CUDA runtime copy call to explicitly move data onto the GPU
    This is called zero-copy (Z-C) GPU-CPU interaction, from where the name “zero-copy memory”
    Calling cudaMemcpy not a must anymore
    Note: data is still red/written through the PCI-E pipe; process managed by the runtime, in a transparent fashion
The device memory ballooned, virtually, to include chunk that physically belongs to the host

## Slide 24: From Z-C to UVA: CUDA 2.2 to CUDA 4.0
Pain in the rear: Z-C enabled access of data on the host from the device required one additional runtime call to cudaHostGetDevicePointer()
  cudaHostGetDevicePointer(): given a pointer to pinned host memory produces a new pointer that can be invoked within the kernel to access data stored on the host
The need for the cudaHostGetDevicePointer() call was eliminated in CUDA 4.0 with the introduction of the Unified Virtual Addressing (UVA) mechanism

## Slide 25: Unified Virtual Address Space: From CUDA programming guide
All host memory allocations made via CUDA API calls and all device memory allocations on supported devices are within the UVAS. As a consequence:
  Today, the location of any memory on any of the devices or on the host allocated through CUDA can be determined from the value of the pointer using cudaPointerGetAttributes()
  When copying to or from the memory of any device the cudaMemcpyKind parameter of cudaMemcpy*() can be set to cudaMemcpyDefault to determine locations from the pointers
  Allocations via cudaHostAlloc() are automatically portable across all the devices
  Pointers returned by cudaHostAlloc() can be used directly from within kernels running on a device
[NVIDIA]

## Slide 26: UVA – Showcasing Its Versatility…
Set of commands below can be issued by one host thread to multiple devices
  No need to use anything beyond cudaMemcpyDefault
    cudaMemcpy(gpu1Dst_memPntr, host_memPntr, byteSize1, cudaMemcpyDefault)
    cudaMemcpy(gpu2Dst_memPntr, host_memPntr, byteSize2, cudaMemcpyDefault)
    cudaMemcpy(host_memPntr, gpu1Dst_memPntr, byteSize1, cudaMemcpyDefault)
    cudaMemcpy(host_memPntr, gpu2Dst_memPntr, byteSize2, cudaMemcpyDefault)
UVA support is the enabler for the peer-to-peer (P2P), inter-GPU, data transfer
  P2P not discussed here
  UVA is the underpinning technology for P2P
Notes: SR: I don’t follow this? A single thread could have done this before. With our without cudaMemcpyHostToDevice (etc.)

## Slide 27: UVA is a Step Forward Relative to Z-C
Z-C Key Accomplishment: use pointer within device function access host data
  Z-C focused on a data access, an issue relevant in the context of functions executed on the device
UVA had a data access component but also a data transfer component:
  Data access: A GPU could access data on a different GPU, a novelty back in CUDA 4.0
  Data transfer: copy data in between GPUs
    cudaMemcpy is the main character in this play, data transfer initiated on the host side

## Slide 28: UVA & Unified Memory (UM)
The Unified Virtual Address idea had ok impact, perhaps good enough to write home about
Unified Memory (UM) took this idea to town by allowing the CPU to tap into GPU memory
  UM works in conjunction with a “managed memory pool”
Fallout: improved significantly CUDA ease of use, particularly for multi-GPU systems

## Slide 29: Unified Memory, a first example
#include <stdio.h>
#include <stdlib.h>
#define SZ 8
__device__ __managed__ int ret[SZ];
__global__ void AplusB(int *ret, int a, int b) {
ret[threadIdx.x] = a + b + threadIdx.x;
}
int main() {
AplusB<<<1, SZ>>>(10, 100);
cudaDeviceSynchronize();
for (int i = 0; i < SZ; i++)
printf("%d: A+B = %d\n", i, ret[i]);
return 0;
}
#include <stdio.h>
#include <stdlib.h>
#define SZ 8
__global__ void AplusB(int *ret, int a, int b) {
ret[threadIdx.x] = a + b + threadIdx.x;
}
int main() {
int *ret;
cudaMallocManaged(&ret, SZ * sizeof(int));
AplusB<<<1, SZ>>>(ret, 10, 100);
cudaDeviceSynchronize();
for (int i = 0; i < SZ; i++)
printf("%d: A+B = %d\n", i, ret[i]);
cudaFree(ret);
return 0;
}
#include <stdio.h>
#include <stdlib.h>
#define SZ 8
__global__ void AplusB(int *ret, int a, int b) {
ret[threadIdx.x] = a + b + threadIdx.x;
}
int main() {
int *ret;
cudaMalloc(&ret, SZ * sizeof(int));
AplusB<<<1, SZ>>>(ret, 10, 100);
int *host_ret = (int *)malloc(SZ * sizeof(int));
cudaMemcpy(host_ret, ret, SZ * sizeof(int), cudaMemcpyDefault);
for (int i = 0; i < SZ; i++)
printf("%d: A+B = %d\n", i, host_ret[i]);
free(host_ret);
cudaFree(ret);
return 0;
}
12 lines of code
8 lines of code
(can make it 7)
10 lines of code
TRUMAN Debug> ./unifMemCUDAexPart1.exe
0: A+B = 110
1: A+B = 111
2: A+B = 112
3: A+B = 113
4: A+B = 114
5: A+B = 115
6: A+B = 116
7: A+B = 117

## Slide 30: Unified Memory: further thoughts
One memory allocation call takes care of memory setup at both ends; i.e., device and host
  The main actor: the CUDA runtime function cudaMallocManaged()
New way of perceiving the memory interplay in GPGPU computing
  No distinction is made between memory on the host and memory on the device
  It’s just a pool of memory, albeit with different access times when accessed by different processors
    “processor”: any independent execution unit with a dedicated memory management unit (MMU)
      Includes both CPUs and GPUs of any type and architecture
Old Memory Perception
New Perception with Unified Memory
[NVIDIA]

## Slide 31: The UM innovation
No longer any need for explicit memory transfers between host and device
  Any allocation created in the managed memory space automatically migrated to where it is needed
Also, UM eliminates the need to call the cudaMalloc/cudaHostAlloc duo
  It takes a different perspective on handling memory in the GPU/CPU interplay

## Slide 32: UM - Other interesting tidbits
Reliance on a managed memory space in which all processors see a single coherent memory image with a common address space
The runtime manages data access and locality within a CUDA program without need for explicit memory copy calls
Memory is migrated where it is used, the page table of the processors is simply updated
One can now oversubscribe the amount of memory on the device
  Allocate more than available; might spill into host memory

## Slide 33: Then and Now: no-UM vs. UM
#include "math.h"
#include <iostream>
const int ARRAY_SIZE = 1000;
using namespace std;
__global__ void increment(double *aArray, double val, unsigned int sz) {
unsigned int indx = blockIdx.x * blockDim.x + threadIdx.x;
if (indx < sz)
aArray[indx] += val;
}
int main(int argc, char **argv) {
double *mA;
cudaMallocManaged(&mA, ARRAY_SIZE * sizeof(double));
for (int i = 0; i < ARRAY_SIZE; i++)
mA[i] = 1. * i;
double inc_val = 2.0;
increment<<<2, 512>>>(mA, inc_val, ARRAY_SIZE);
cudaDeviceSynchronize();
double error = 0.;
for (int i = 0; i < ARRAY_SIZE; i++)
error += fabs(mA[i] - (i + inc_val));
cout << "Test: " << (error < 1.E-9 ? "Passed" : "Failed") << endl;
cudaFree(mA);
return 0;
}
#include "math.h"
#include <iostream>
const int ARRAY_SIZE = 1000;
using namespace std;
__global__ void increment(double *aArray, double val, unsigned int sz) {
unsigned int indx = blockIdx.x * blockDim.x + threadIdx.x;
if (indx < sz)
aArray[indx] += val;
}
int main(int argc, char **argv) {
double *hA;
double *dA;
hA = (double *)malloc(ARRAY_SIZE * sizeof(double));
cudaMalloc(&dA, ARRAY_SIZE * sizeof(double));
for (int i = 0; i < ARRAY_SIZE; i++)
hA[i] = 1. * i;
double inc_val = 2.0;
cudaMemcpy(dA, hA, sizeof(double) * ARRAY_SIZE, cudaMemcpyHostToDevice);
increment<<<2, 512>>>(dA, inc_val, ARRAY_SIZE);
cudaMemcpy(hA, dA, sizeof(double) * ARRAY_SIZE, cudaMemcpyDeviceToHost);
double error = 0.;
for (int i = 0; i < ARRAY_SIZE; i++)
error += fabs(hA[i] - (i + inc_val));
cout << "Test: " << (error < 1.E-9 ? "Passed" : "Failed") << endl;
cudaFree(dA);
free(hA);
return 0;
}

## Slide 34: Requirements, UM
GPU with SM architecture 3.0 or higher (Kepler class or newer)
A 64-bit host application and non-embedded operating system (Linux, Windows, macOS)
CUDA 6.0 or higher
NOTE: UM is very much work in progress, not all features supported on Windows or MacOS
  Linux kernel has good support for UM

## Slide 35: UM vs. Z-C
Recall that with Z-C, data is always on the host in pinned CPU system memory
  The device can update data on the host (if host memory pinned), but not vice-versa
UM: data stored on the device but migrated where needed
  Data access and locality managed by CUDA runtime, handling transparent to the user
  UM provides “single-pointer-to-data” model
  The host can finally modify data that is stored on the device
    Before, the host could drop data in device memory, but not directly modify it

## Slide 36: UM: Required API Changes
As far as the CUDA API is concerned, UM led to *three* new family members :
  cudaMallocManaged
  __managed__
  cudaStreamAttachMemAsync()
There is a lot more that doesn’t meet the eye. Very tough nut to crack, managed memory

## Slide 37: cudaMallocManaged
Function Prototype:
cudaError_t cudaMallocManaged(void** devPtr, size_t size, unsigned int flag)
  A drop-in replacement for cudaMalloc() – they are semantically identical
  Allocates managed memory on the device
  First two arguments have the expected meaning
  Caveats:
    devPtr: pointer accessible from both Host and Device
    flag controls the default stream association for this allocation
      cudaMemAttachGlobal - memory is accessible from any stream on any device
      cudaMemAttachHost – memory on this device accessible by host only
  Free memory with the same cudaFree()

## Slide 38: __managed__
Global/file-scope variable annotation combines with __device__
Declares global-scope migrate-able device variable
Symbol accessible from both GPU and CPU code
#include <stdio.h>
#include <stdlib.h>
#define SZ 8
__device__ __managed__ int ret[SZ];
__global__ void AplusB(int a, int b) {
ret[threadIdx.x] = a + b + threadIdx.x;
}
int main() {
AplusB<<<1, SZ>>>(10, 100);
cudaDeviceSynchronize();
for (int i = 0; i < SZ; i++)
printf("%d: A+B = %d\n", i, ret[i]);
return 0;
}

## Slide 39: cudaStreamAttachMemAsync()
Manages concurrency in multi-threaded CPU applications
Not relevant here

## Slide 40: UM, other quick points
Managed memory is interoperable and interchangeable with device-specific allocations, such as those created using the cudaMalloc() routine
  Translation:
    cudaMallocManaged()– allocated memory behaves in all situations like memory allocated with cudaMalloc()
    But not vice-versa
All CUDA operations that are valid on device memory are also valid on managed memory

## Slide 41: UM, other quick points
On Pascal and later GPUs, managed memory might not be physically allocated when cudaMallocManaged() returns
  It may only be populated on access (or prefetching)
    Page table entries and memory frames might not be created until they are accessed by the GPU or the CPU
  The pages can migrate to any processor’s memory at any time, and the CUDA runtime employs heuristics to maintain data locality and prevent excessive page faults
[https://devblogs.nvidia.com/unified-memory-cuda-beginners]

## Slide 42: UM, Nuts and Bolts
Managed memory migration is at the page level
  The default page size is currently the same as the OS page size today (typically 4 KiB)
The runtime intercepts CPU dirty pages and detects page faults
  Moves from device over PCI-E only the dirty pages
  Transparently, pages touched by the CPU (GPU) are moved back to the device (host) when needed
Notes: A lot of this picked up from http://devblogs.nvidia.com/parallelforall/unified-memory-in-cuda-6/

## Slide 43: UM, Nuts and Bolts
Simultaneous access to managed memory from the CPU & GPUs with CC<6.0 not possible
  Pre-Pascal GPUs lack hardware page faulting, so coherence can’t be guaranteed
  Therefore, if CC<6.0, an access from the CPU while a kernel is running will cause a segmentation fault
On Pascal and later GPUs, the CPU & the GPU can simultaneously access managed memory, since they can both handle page faults
  NOTE: up to application developer to ensure there are no race conditions caused by simultaneous accesses
Notes: A lot of this picked up from http://devblogs.nvidia.com/parallelforall/unified-memory-in-cuda-6/

## Slide 44: UM: Access to managed memory pool
Playing it safe: use cudaDeviceSynchronize() before having the host work on memory that the GPU is also working on
Note: Any function that logically guarantees the GPU finished execution is actually acceptable
  Examples: cudaStreanSynchronize(), cudaMemcpy(), cudaMemset(), etc.

## Slide 45: UM: Access to managed pool – Example, for CC<6.0
__device__ __managed__ int x, y = 2;
__global__ void kernel() {
x = 10;
}
int main() {
kernel << < 1, 1 >> >();
y = 20; // ERROR: CPU access concurrent with GPU
cudaDeviceSynchronize();
return 0;
}
__device__ __managed__ int x, y = 2;
__global__ void kernel() {
x = 10;
}
int main() {
kernel << < 1, 1 >> >();
cudaDeviceSynchronize();
y = 20; // GPU is idle so access is OK
return 0;
}
[NVIDIA, Programming Guide]
Bad: Execution seg. faults
Good: Code runs ok

## Slide 46: Unified Memory, under the hood
 | page1 |  | page2 |  | 
Single virtual memory shared between processors
[Nikolay Sakharnykh]
GPU A
(better yet, processor A)
GPU B
(better yet, processor B)

## Slide 47: Unified Memory, under the hood
page1
page2
GPU A
(better yet, processor A)
A’s page table
A’s phys mem
B’s phys mem
page1
page2
B’s page table
All processors operate in/perceive one single virtual memory. The physical memory is a odd thing
 | page1 |  | page2 |  | 
[Nikolay Sakharnykh]
GPU B
(better yet, processor B)
The virtual
memory

## Slide 48: Unified Memory, under the hood
page1
page2
page3
A’s phys mem
B’s phys mem
page1
page2
page3
*addr1 = 1
local access
*addr3 = 1 page fault
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 49: Unified Memory, under the hood
page1
page2
page3
A’s phys mem
B’s phys mem
*addr3 = 1 access replay
page3 populated and mapped into B’s memory
A’s page table
B’s page table
[Nikolay Sakharnykh]
page 3
page 2
page 1

## Slide 50: Unified Memory, under the hood
page1
page2
page3
A’s phys mem
B’s phys mem
page1
page2
page3
*addr2 = 1 page fault
*addr3 = 7
page fault
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 51: Unified Memory, under the hood
page1
page2
page3
A’s phys mem
B’s phys mem
page1
page2
page3
*addr2 = 1 page fault
*addr3 = 7
page fault
page2 and page3 unmapped from B’s memory
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 52: Unified Memory, under the hood
page1
page2
page3
A’s phys mem
B’s phys mem
page1
page2
page3
*addr2 = 1 page fault
*addr3 = 7
page fault
pages data migrated to A’s physical memory
A’s page table
B’s page table
[Nikolay Sakharnykh]
migration
(runtime managed)

## Slide 53: Unified Memory, under the hood
page1
page2
page3
A’s phys mem
B’s phys mem
page1
page2
page3
*addr2 = 1 access replay
*addr3 = 7
access replay
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 54: Unified Memory, under the hood
page1
page2
page3
page4
A’s phys mem
B’s phys mem
page1
page2
page3
page4
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 55: Unified Memory, under the hood
page1
page2
page3
page4
page5
A’s phys mem
B’s phys mem
page1
page2
page3
page4
page5
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 56: Unified Memory, under the hood
page1
page2
page3
page4
page5
A’s phys mem
B’s phys mem
page1
page2
page3
page4
page5
*addr5 = 9
page fault
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 57: Unified Memory, under the hood
page1
page2
page3
page4
page5
A’s phys mem
B’s phys mem
page1
page2
page3
page4
page5
*addr5 = 9
page fault
page4 unmapped from A’s memory and migrated
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 58: Unified Memory, under the hood
page1
page2
page3
page4
page5
A’s phys mem
B’s phys mem
page1
page2
page3
page4
page5
*addr5 = 9
page fault
page4 mapped in B’s memory, page5 unmapped and migrated to A
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 59: Unified Memory, under the hood
page1
page2
page3
page4
page5
A’s phys mem
B’s phys mem
page1
page2
page3
page4
page5
*addr5 = 9
access replay
A’s page table
B’s page table
[Nikolay Sakharnykh]

## Slide 60: UM level of support
Linux is most mature in UM support
  E.g.: additional Unified Memory features on Linux (only)
    On-demand page migration
    GPU memory oversubscription
Windows and MacOS support UM but not have the two features above

## Slide 61: Unified Memory platforms
 | KEPLER | PASCAL | VOLTA
Linux + x86 | No GPU fault support No concurrent access | On-demand migration | On-demand migration
Linux + Power 9 |  | On-demand migration 80GB/s CPU-GPU BW | On-demand migration 150GB/s CPU-GPU BW Access counters HW coherency ATS support
Windows | No GPU fault support No concurrent access |  | 
MacOS | No GPU fault support No concurrent access |  | 
Tegra | Cached on CPU and iGPU No concurrent access |  | 
 | KEPLER | PASCAL | VOLTA
Linux + x86 | No GPU fault support No concurrent access | On-demand migration | On-demand migration
Linux + Power 9 |  |  | 
Windows | No GPU fault support No concurrent access |  | 
MacOS | No GPU fault support No concurrent access |  | 
Tegra | Cached on CPU and iGPU No concurrent access |  | 
[Nikolay Sakharnykh]

## Slide 62: CUDA + Power 9 on Euler
#include <stdio.h>
#include <stdlib.h>
#define SZ 8
__global__ void AplusB(int a, int b, int* result){
result[threadIdx.x] = a + b + threadIdx.x;
}
int main() {
int ret[SZ];
AplusB <<<1, SZ >>>(10, 100, ret);
cudaDeviceSynchronize();
for (int i = 0; i < SZ; i++)
printf("%d: A+B = %d\n", i, ret[i]);
return 0;
}
me759@euler ~/t/cuda> nvprof ./ats_static
==19313== NVPROF is profiling process 19313, command: ./ats_static
0: A+B = 110
1: A+B = 111
2: A+B = 112
3: A+B = 113
4: A+B = 114
5: A+B = 115
6: A+B = 116
7: A+B = 117
==19313== Profiling application: ./ats_static
==19313== Profiling result:
Type Time(%) Time Calls Avg Min Max Name
GPU activities: 100.00% 5.5040us 1 5.5040us 5.5040us 5.5040us AplusB(int, int, int*)
API calls: 98.68% 196.71ms 1 196.71ms 196.71ms 196.71ms cudaLaunchKernel
0.83% 1.6498ms 1 1.6498ms 1.6498ms 1.6498ms cuDeviceTotalMem
0.44% 884.81us 96 9.2160us 199ns 357.96us cuDeviceGetAttribute
0.04% 76.012us 1 76.012us 76.012us 76.012us cuDeviceGetName
0.00% 8.8440us 1 8.8440us 8.8440us 8.8440us cudaDeviceSynchronize
0.00% 2.6110us 1 2.6110us 2.6110us 2.6110us cuDeviceGetPCIBusId
0.00% 1.9410us 3 647ns 363ns 1.0430us cuDeviceGetCount
0.00% 1.1720us 2 586ns 326ns 846ns cuDeviceGet
0.00% 316ns 1 316ns 316ns 316ns cuDeviceGetUuid

## Slide 63: CUDA & Power 9
void *data;
data = malloc(N);
cpu_func1(data, N); cpu_func2(data, N);
cpu_func3(data, N); free(data);
void *data;
data = malloc(N);
cpu_func1(data, N);
gpu_func2<<<...>>>(data, N);
cudaDeviceSynchronize();
cpu_func3(data, N);
free(data);
CPU code
CPU vs GPU
GPU code w/ Unified Memory
[Nikolay Sakharnykh]
This function call not needed if synchronous kernel calls

## Slide 64: CUDA & Power 9
cudaMalloc(&d_data, N);
cudaMemcpy(d_data, data, N, ...)
gpu_func2<<<...>>>(d_data, N); cudaMemcpy(data, d_data, N, ...) cudaFree(d_data);
void *data;
data = malloc(N);
cpu_func1(data, N);
gpu_func2<<<...>>>(data, N); cudaDeviceSynchronize();
cpu_func3(data, N); free(data);
Explicit mem. Management vs. Unified Memory
Explicit Memory Management GPU code w/ Unified Memory
void *data, *d_data; data = malloc(N);
cpu_func1(data, N);
cpu_func3(data, N); free(data);
[Nikolay Sakharnykh]

## Slide 65: CUDA & Power 9
void *data, *d_data;
data = malloc(N); cudaMalloc(&d_data, N); cpu_func1(data, N); cudaMemcpy(d_data, data, N, ...) gpu_func2<<<...>>>(d_data, N); cudaMemcpy(data, d_data, N, ...) cudaFree(d_data); cpu_func3(data, N);
free(data);
cudaMemPrefetchAsync(data, N, GPU)
cudaMemPrefetchAsync(data, N, CPU)
Full Control with Prefetching
Explicit Memory Management Unified Memory + Prefetching
void *data; data = malloc(N); cpu_func1(data, N);
gpu_func2<<<...>>>(data, N);
cudaDeviceSynchronize(); cpu_func3(data, N); free(data);
[Nikolay Sakharnykh]

## Slide 66: CUDA & Power 9
char **data;
// allocate and initialize data on the CPU
char **d_data;
char **h_data = (char**)malloc(N*sizeof(char*)); for (int i = 0; i < N; i++) {
cudaMalloc(&h_data[i], N);
cudaMemcpy(h_data[i], data[i], N, ...);
}
cudaMalloc(&d_data, N*sizeof(char*)); cudaMemcpy(d_data, h_data, N*sizeof(char*), ...);
gpu_func<<<...>>>(d_data, N);
char **data;
// allocate and initialize data on the CPU
gpu_func<<<...>>>(data, N);
Deep Copy
Explicit Memory Management GPU code w/ Unified Memory
[Nikolay Sakharnykh]

## Slide 67: UM – Why Bother?
  A matter of convenience
    Much simpler to write code using this memory model
    For the casual programmer, the code will probably run faster due to data locality
      The CUDA runtime will take care of moving the data where it ought to be
  Looking ahead, we’ll see more of this in the next 18 – 24 months
    Already the case for integrated GPUs that are part of the system chipset (Tegra Xavier)
    Better support coming for Windows & MacOS

## Slide 68: High vantage point, the big picture
In the beginning the host and device memory spaces were totally separated
Then, the device could access memory on the host (Z-C memory access)
Then, the idea of a unified virtual space took off and we had UVA
  P2P communication, no need for pointer de-mangling
Finally, the UM (managed memory) came along; processors can access each other’s memory
  The field is in flux

## Slide 69: GPU Computing with thrust

## Slide 70: Three Ways to Accelerate on GPU
Libraries
Directives
Programming Languages
Application
Easiest Approach
Maximum Performance
Direction of increased performance
(and effort)
NVIDIA [C. Woolley]→
Notes: On the NVIDIA website, Thrust is listed under “Libraries” (https://developer.nvidia.com/gpu-accelerated-libraries).

## Slide 71: Acknowledgments
The thrust slides include material provided by Nathan Bell previously of NVIDIA (at Google now)
Slightly modified, assuming responsibility for any mistakes

## Slide 72: Design Philosophy, thrust
Increase programmer productivity
  Build applications quickly via generic programming
    Leverage a template-based approach.
Should run fast
  Efficient mapping to hardware
NVIDIA [N. Bell]→

## Slide 73: What is thrust?
A template library for parallel computing on GPU and CPU*
  Mimics the C++ STL
Heavy use of C++ containers
Provides ready to use generic algorithms
  Sorting, reduction, scan, etc.
NVIDIA [N. Bell]→

## Slide 74: What is thrust?
thrust is a header library
  All its functionality accessed by #include-ing the appropriate thrust header file
Program is compiled with nvcc as per usual, no special tools are required
Heavy-duty C++ syntax. Related to high-level, host-side code that you write
  The concept of execution configuration, shared memory, etc. : it’s all gone
NVIDIA [N. Bell]→

## Slide 75: A First Example
NVIDIA [N. Bell]→
#include <thrust/host_vector.h>
#include <thrust/device_vector.h>
#include <thrust/sort.h>
int main(void) {
// generate about 16M random numbers on the host
thrust::host_vector<int> h_vec(1 << 24);
thrust::generate(h_vec.begin(), h_vec.end(), rand);
// transfer data to the device
thrust::device_vector<int> d_vec = h_vec;
// sort data on the device
thrust::sort(d_vec.begin(), d_vec.end());
// transfer data back to host
thrust::copy(d_vec.begin(), d_vec.end(), h_vec.begin());
return 0;
}
Notes: the = operator can be used to copy a host_vector to a device_vector (or vice-versa). The = operator can also be used to copy host_vector to host_vector or device_vector to device_vector.
this is a complete Thrust program
Thrust is a header library – all the functionality is accessed by #including the appropriate Thrust header file
This program is compiled with nvcc as per usual, no special tools are required