## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2020]
Lecture 05
01/31/2019
Dan Negrut, 2020 ME759 UW-Madison

## Slide 2: Quote of the day
“English? Who needs that? I'm never going to England.”
-- Homer Simpson, Safety Inspector, anticipating Brexit [1989 - ]

## Slide 3: Before we get going…
Last time: the Hardware Software interplay
  Thread Level Parallelism (TLP)
  Measuring execution performance, quick thoughts
  The memory hierarchy
Today
  The Cache
  The virtual memory
Other tidbits:
  Please take care of the assigned reading
  Another assignment went out, due Th at 9 pm
  Use Piazza to get things going (for you or others)

## Slide 4: Memory Speed: Widening of the Processor-DRAM Speed Gap
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fourth edition
Notes: QUESTION: we talk about memory wall as an impediment to continuing increase in sequential computing performance and we said that the problem is that memory cannot keep up feeding the raw number crunching capability of the CPU.
But then, how can parallel computing be the answer? How could memory serve now multiple “consumers” and yet overall performance increase?
To explain this, we note that memory performance is related to two key concepts:
latency
bandwidth

## Slide 5: Cache Memories
Cache memories are small, fast, on-chip SRAM-based memories
  Purpose: to store close to the CU/ALU frequently accessed blocks of main, or system, memory
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory
[Bryant and O‘Hallaron: CMU] →

## Slide 6: What it Really Looks Like
Source: Dell
Desktop PC
[Bryant and O‘Hallaron: CMU] →
Source: Dell
Motherboard
Source: Dell
Main memory (DRAM)
Source: PC Magazine
Source: techreport.com
CPU (Intel Core i7)
Gets dropped in here

## Slide 7: What it Really Looks Like [contd.]
[Bryant and O‘Hallaron: CMU] →
Bus interface
ALU
Register file
CPU chip
Cache
memory
Intel Sandy Bridge-E
Processor Die
[8 core-version]
L1: 32KB Instruction + 32KB Data
L2: 256KB
L3: 5–20MB

## Slide 8: How Cache Comes into Play
All* read/write operations go through cache
Caches used to hold both data and instructions
  Data and instructions caches are in general different
    Intel: L1 DC (data cache) and L1 IC (instruction cache) have been distinct since of 1993
Main Memory
Cache
CPU Core
Bus

## Slide 9: Caches: Come In Two Flavors
Data caches feed processor with data manipulated during execution
  If processor would rely on data provided by main memory the execution would be pitifully slow
    “Processor Clock” much faster than the “Memory Clock”
      Caches alleviate the memory pressure – processors are data hungry
Instruction caches: used to store instructions
  Simpler to deal with compared to the data caches
    By and large, instruction use is much more predictable than data use

## Slide 10: Processor Clock vs. Memory Clock
Processor Clock: (look for the box )
  Dictates/defines the frequency at which Functional Units operate
Memory Clock:
  Dictates/defines the frequency used to move data into/out from main memory into cache
From RAM
To/From RAM

## Slide 11: Caches: How large? Also, how fast?
Ratio between cache size and main memory size
  Reasonable to expect something like 1:1000
    2013: 4 MB of L3 cache, versus 4 GB of main memory
    2017: 55 MB of L3 cache, versus 64 GB of main memory
Vintage: 2013 (related to Intel’s Haswell)
Latency in Clocks –Lower is Better
(log scale)
This chip has L4 cache, read more about it here
This is the overhead of a system memory access (about 100+ cycles)

## Slide 12: Multiple Levels of Cache
Commodity chips today have 3 cache levels
  (some chips have a fourth cache level, see previous slide)
Main Memory
L3 Cache
Bus
L2 Cache
L1 D$
CPU Core
L1 I$

## Slide 13: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 7
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way assoc.
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way assoc.
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way assoc.
  Access: 40-75 cycles
Block size: 64 bytes for all caches.
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 14: Why Caches Work: the “Principle of Locality”
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  “Recently referenced items are likely to be referenced again in the near future”
Spatial locality:
  “Items with nearby addresses tend to come into use together”
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 15: Spatial and Temporal Locality
Temporal Locality for memory access by a program
  Idea: If you access a variable at some time, then you’ll probably keep accessing the same variable for a while
    Example: a for loop with some variables inside the loop  you keep accessing those variables as long as you loop
Spatial Locality for memory access by a program
  A memory access pattern characterized by bursts of repeated requests for data that is physically located within the same memory region
  “Bursts” because these accesses should happen in a sufficiently short interval of time (lest the cache line gets evicted)

## Slide 16: Example, regarding concept of “locality”
Data references
  Reference array a elements in succession (stride-1 reference pattern) spatial locality
  Reference variable sum each iteration temporal locality
Instruction references
  Reference instructions in sequence spatial locality
  Cycle through loop repeatedly temporal locality
// some simple code snippet
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 17: Example: Adding the Entries in a 2D Matrix
Example used over several slides to show how “locality” and caches impact performance
Very related to your second assignment

## Slide 18: Example [motivation]: Adding the Entries in a 2D Matrix
Two equivalent ways to add the entries in a matrix
Row-wise:
Column-wise:
Example used over several slides to show how “locality” and caches impact performance
Second row
First row
First column
Second column
Third column

## Slide 19: Squashed format vs. 2D format
Storing a matrix: squashed format OR 2D format
Example:
Squashed format – using one long contiguous array of 6 entries. Like in your homework
The 2D format – using two arrays:
  Each has 3 entries
  Each of the two arrays stored somewhere in the memory (they might be far from each other)

## Slide 20: First way to represent 2D matrix: the “squashed,” 1D approach
One long array stores all entries in the matrix
  E.g., a 23 matrix will have an array of size 6
2D matrix stored in 1D array, row-wise fashion
  All the entries in the first row are stored first, followed by the entries in the second row, which are followed by the matrix in the third row, etc.
Note that we use malloc once
  We’ll have to use free once when we’re done
Windows executable called “matrix1D.exe”
#include <stdio.h>
#include <stdlib.h>
struct squashedMatrix {
/// 2D matrix stored row-wise in a one dimensional array
unsigned int height; /// number of rows in matrix
unsigned int width; /// number of columns in matrix
double *pMatVals;
};
int main() {
struct squashedMatrix mat1D;
mat1D.height = 1000; // perhaps you set this based on user input
mat1D.width = 2000; // perhaps you set this based on user input
mat1D.pMatVals = (double *)malloc(mat1D.height * mat1D.width * sizeof(double));
unsigned int i, j;
for (i = 0; i < mat1D.height; i++)
for (j = 0; j < mat1D.width; j++)
mat1D.pMatVals[i * mat1D.width + j] = 1. / (i + j + 1.);
// Compute sum of elements
double sum = 0.;
for (i = 0; i < mat1D.height; i++)
for (j = 0; j < mat1D.width; j++)
sum += mat1D.pMatVals[i * mat1D.width + j];
printf("The sum of the elements is: %f\n", sum);
// Done with the matrix; free the mem
free(mat1D.pMatVals);
return 0;
}

## Slide 21: A second way to represent the 2D matrix: the 2D approach
First we allocate room to store a number of pointers to double
  There are “height” of these “double *” pointers
  These pointers stored in the array pRows
For each matrix row (and there are “height” of them), we allocate enough room to store “width” doubles
  These are the values that show up in a row of the matrix
Note that I use malloc multiple times
  We’ll have to use free multiple times
Windows executable called “matrix2D.exe”
#include <stdio.h>
#include <stdlib.h>
struct Matrix2D {
/// 2D matrix stored row-wise in a one dimensional array
unsigned int height; /// number of rows in matrix
unsigned int width; /// number of columns in matrix
double **pRows;
};
int main() {
struct Matrix2D mat2D;
mat2D.height = 1000; // perhaps you set this based on user input
mat2D.width = 2000; // perhaps you set this based on user input
mat2D.pRows = (double **)malloc(mat2D.height * sizeof(double *));
unsigned int i;
for (i = 0; i < mat2D.height; i++)
mat2D.pRows[i] = (double *)malloc(mat2D.width * sizeof(double));
// Get meaningful values in this matrix
unsigned int j;
for (i = 0; i < mat2D.height; i++)
for (j = 0; j < mat2D.width; j++)
mat2D.pRows[i][j] = 1. / (i + j + 1.);
// Compute sum of elements
double sum = 0;
for (i = 0; i < mat2D.height; i++)
for (j = 0; j < mat2D.width; j++)
sum += mat2D.pRows[i][j];
printf("The sum of the elements is: %f\n", sum);
// Don't data anymore, free mem; note that free is used twice
for (i = 0; i < mat2D.height; i++)
free(mat2D.pRows[i]);
free(mat2D.pRows);
return 0;
}

## Slide 22: The squashed approach, revisited: locality vs. non-locality
#include <Windows.h> // need this for timing
#include <stdio.h>
#include <stdlib.h>
struct squashedMatrix {
/// 2D matrix stored row-wise in a one dimensional array
unsigned int height; /// number of rows in matrix
unsigned int width; /// number of columns in matrix
double *pMatVals;
};
int main(int argc, char *argv[]) {
if (argc != 2) {
printf("Pass 1 for row-wise, pass 2 for column-wise sum.\n");
return 1;
}
int option = atoi(argv[1]);
struct squashedMatrix mat1D;
mat1D.height = 2000; // perhaps you set this based on user input
mat1D.width = 2000; // perhaps you set this based on user input
mat1D.pMatVals = (double *)malloc(mat1D.height * mat1D.width * sizeof(double));
unsigned int i, j;
for (i = 0; i < mat1D.height; i++)
for (j = 0; j < mat1D.width; j++)
mat1D.pMatVals[i * mat1D.width + j] = 1. / (i + j + 1.);
// Compute sum of elements
double sum = 0.;
__int64 ctr1 = 0, ctr2 = 0, freq = 0; // need this for timing
if (QueryPerformanceCounter((LARGE_INTEGER *)&ctr1) != 0) {
if (option == 1) {
for (i = 0; i < mat1D.height; i++)
for (j = 0; j < mat1D.width; j++)
sum += mat1D.pMatVals[i * mat1D.width + j];
} else if (option == 2) {
for (j = 0; j < mat1D.width; j++) {
for (i = 0; i < mat1D.height; i++)
sum += mat1D.pMatVals[i * mat1D.width + j];
}
} else {
printf("Bad input option.\n");
return 1;
}
QueryPerformanceCounter((LARGE_INTEGER *)&ctr2);
QueryPerformanceFrequency((LARGE_INTEGER *)&freq);
}
printf("The sum of the elements is: %f\n", sum);
printf("Time spent in microseconds: %f\n", (ctr2 - ctr1) * 1.0 / freq);
// Done with the matrix; free the mem
free(mat1D.pMatVals);
return 0;
}

## Slide 23: Results, release build: 6 to 7 times faster if accessed w/ locality
TRUMAN Release> ./matrixRep1D.exe
Pass 1 for row-wise, pass 2 for column-wise sum.
TRUMAN Release>
TRUMAN Release>
TRUMAN Release> ./matrixRep1D.exe 1
The sum of the elements is: 2772.088785
Time spent in microseconds: 0.003622
TRUMAN Release>
TRUMAN Release>
TRUMAN Release> ./matrixRep1D.exe 2
The sum of the elements is: 2772.088785
Time spent in microseconds: 0.023060
TRUMAN Release>
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)

## Slide 24: The 2D approach, revisited: locality vs. non-locality
#include <Windows.h> // need this for timing
#include <stdio.h>
#include <stdlib.h>
struct Matrix2D {
/// 2D matrix stored row-wise in a one dimensional array
unsigned int height; /// number of rows in matrix
unsigned int width; /// number of columns in matrix
double **pRows;
};
int main(int argc, char *argv[]) {
if (argc != 2) {
printf("Pass 1 for row-wise, pass 2 for column-wise sum.\n");
return 1;
}
int option = atoi(argv[1]);
struct Matrix2D mat2D;
mat2D.height = 2000; // perhaps you set this based on user input
mat2D.width = 2000; // perhaps you set this based on user input
mat2D.pRows = (double **)malloc(mat2D.height * sizeof(double *));
unsigned int i;
for (i = 0; i < mat2D.height; i++)
mat2D.pRows[i] = (double *)malloc(mat2D.width * sizeof(double));
// Get meaningful values in this matrix
unsigned int j;
for (i = 0; i < mat2D.height; i++)
for (j = 0; j < mat2D.width; j++)
mat2D.pRows[i][j] = 1. / (i + j + 1.);
// Compute sum of elements
double sum = 0;
__int64 ctr1 = 0, ctr2 = 0, freq = 0; // need this for timing
if (QueryPerformanceCounter((LARGE_INTEGER *)&ctr1) != 0) {
if (option == 1) {
for (i = 0; i < mat2D.height; i++)
for (j = 0; j < mat2D.width; j++)
sum += mat2D.pRows[i][j];
} else if (option == 2) {
for (j = 0; j < mat2D.width; j++)
for (i = 0; i < mat2D.height; i++)
sum += mat2D.pRows[i][j];
} else {
printf("Bad input option.\n");
return 1;
}
QueryPerformanceCounter((LARGE_INTEGER *)&ctr2);
QueryPerformanceFrequency((LARGE_INTEGER *)&freq);
}
printf("The sum of the elements is: %f\n", sum);
printf("Time spent in microseconds: %f\n", (ctr2 - ctr1) * 1.0 / freq);
// Don't data anymore, free mem; note that free is used twice
for (i = 0; i < mat2D.height; i++)
free(mat2D.pRows[i]);
free(mat2D.pRows);
return 0;
}

## Slide 25: Results, release build: 5 times faster if accessed w/ locality
TRUMAN Release> ./matrixRep2D.exe
Pass 1 for row-wise, pass 2 for column-wise sum.
TRUMAN Release>
TRUMAN Release>
TRUMAN Release> ./matrixRep2D.exe 1
The sum of the elements is: 2772.088785
Time spent in microseconds: 0.004075
TRUMAN Release>
TRUMAN Release>
TRUMAN Release> ./matrixRep2D.exe 2
The sum of the elements is: 2772.088785
Time spent in microseconds: 0.020078
TRUMAN Release>
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)

## Slide 26: The two scenarios, side by side: squashed and proper 2D
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)
TRUMAN Release> ./matrixRep2D.exe
Pass 1 for row-wise, pass 2 for column-wise sum.
TRUMAN Release>
TRUMAN Release>
TRUMAN Release> ./matrixRep2D.exe 1
The sum of the elements is: 2772.088785
Time spent in microseconds: 0.004075
TRUMAN Release>
TRUMAN Release>
TRUMAN Release> ./matrixRep2D.exe 2
The sum of the elements is: 2772.088785
Time spent in microseconds: 0.020078
TRUMAN Release>
TRUMAN Release> ./matrixRep1D.exe
Pass 1 for row-wise, pass 2 for column-wise sum.
TRUMAN Release>
TRUMAN Release>
TRUMAN Release> ./matrixRep1D.exe 1
The sum of the elements is: 2772.088785
Time spent in microseconds: 0.003622
TRUMAN Release>
TRUMAN Release>
TRUMAN Release> ./matrixRep1D.exe 2
The sum of the elements is: 2772.088785
Time spent in microseconds: 0.023060
TRUMAN Release>

## Slide 27: Final Exam type question: Qualitative Estimates of Locality
Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer
Question: Below, do we have good locality with respect to array a?
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
int sum_array_rows(int** a)
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 28: Final Exam type question: Qualitative Estimates of Locality
Question: Does this function have good locality with respect to array a?
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
int sum_array_cols(int** a)
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 29: Taking it to the next level: 3D Matrices – good locality
#include<iostream>
#include<Windows.h> // need this for timing
int main() {
const int M = 700;
__int64 ctr1 = 0, ctr2 = 0, freq = 0; // need this for timing
double*** bPPP; // use this to store values
bPPP = (double***)malloc(M * sizeof(double**));
for (int i = 0; i < M; i++) {
bPPP[i] = (double**)malloc(M * sizeof(double*));
for (int j = 0; j < M; j++) {
bPPP[i][j] = (double*)malloc(M * sizeof(double));
for (int k = 0; k < M; k++)
bPPP[i][j][k] = 1. / (i + j + k + 1.); // storing some smallish number
}
}
double sum = 0.;
if (QueryPerformanceCounter((LARGE_INTEGER *)&ctr1) != 0) {
// sum up all entries in 3D array
for (int i = 0; i < M; i++)
for (int j = 0; j < M; j++)
for (int k = 0; k < M; k++)
sum += bPPP[i][j][k];
QueryPerformanceCounter((LARGE_INTEGER *)&ctr2);
QueryPerformanceFrequency((LARGE_INTEGER *)&freq);
}
std::cout << "Sum is: " << sum << std::endl;
std::cout << "Time spent in microseconds: " << ((ctr2 - ctr1) * 1.0 / freq) << std::endl;
return 0;
}
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)

## Slide 30: Taking it to the next level: 3D Matrices – bad locality
#include<iostream>
#include<Windows.h> // need this for timing
int main() {
const int M = 700;
__int64 ctr1 = 0, ctr2 = 0, freq = 0; // need this for timing
double*** bPPP; // use this to store values
bPPP = (double***)malloc(M * sizeof(double**));
for (int i = 0; i < M; i++) {
bPPP[i] = (double**)malloc(M * sizeof(double*));
for (int j = 0; j < M; j++) {
bPPP[i][j] = (double*)malloc(M * sizeof(double));
for (int k = 0; k < M; k++)
bPPP[i][j][k] = 1. / (i + j + k + 1.); // storing some smallish number
}
}
double sum = 0.;
if (QueryPerformanceCounter((LARGE_INTEGER *)&ctr1) != 0) {
// sum up all entries in 3D array
for (int k = 0; k < M; k++)
for (int j = 0; j < M; j++)
for (int i = 0; i < M; i++)
sum += bPPP[i][j][k];
QueryPerformanceCounter((LARGE_INTEGER *)&ctr2);
QueryPerformanceFrequency((LARGE_INTEGER *)&freq);
}
std::cout << "Sum is: " << sum << std::endl;
std::cout << "Time spent in microseconds: " << ((ctr2 - ctr1) * 1.0 / freq) << std::endl;
return 0;
}
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)

## Slide 31: Running the code in Debug vs. Release mode: big difference?
#include<iostream>
#include<Windows.h> // need this for timing
int main() {
const int M = 700;
__int64 ctr1 = 0, ctr2 = 0, freq = 0; // need this for timing
double*** bPPP; // use this to store values
bPPP = (double***)malloc(M * sizeof(double**));
for (int i = 0; i < M; i++) {
bPPP[i] = (double**)malloc(M * sizeof(double*));
for (int j = 0; j < M; j++) {
bPPP[i][j] = (double*)malloc(M * sizeof(double));
for (int k = 0; k < M; k++)
bPPP[i][j][k] = 1. / (i + j + k + 1.); // storing some smallish number
}
}
double sum = 0.;
if (QueryPerformanceCounter((LARGE_INTEGER *)&ctr1) != 0) {
// sum up all entries in 3D array
for (int i = 0; i < M; i++)
for (int j = 0; j < M; j++)
for (int k = 0; k < M; k++)
sum += bPPP[i][j][k];
QueryPerformanceCounter((LARGE_INTEGER *)&ctr2);
QueryPerformanceFrequency((LARGE_INTEGER *)&freq);
}
std::cout << "Sum is: " << sum << std::endl;
std::cout << "Time spent in microseconds: " << ((ctr2 - ctr1) * 1.0 / freq) << std::endl;
return 0;
}
OS Name Microsoft Windows 10 Enterprise 2016 LTSB
System Type x64-based PC
Processor Intel(R) Core(TM) i7-6800K CPU @ 3.40GHz, 3401 Mhz, 6 Core(s), 12 Logical Processor(s)
Installed Physical Memory (RAM) 32.0 GB
Compiler Visual Studio 2015 (Enterprise)
“Debug” mode
“Release” mode

## Slide 32: Three observations related to our 2D and 3D examples
Observation 1: Final value for sum - stays the same (at least as far as we can tell)
  We’ll talk more about this when we do parallel computing w/ CUDA and then OpenMP
Observation 2: Difference between Debug vs Release builds
  3X to 4X speedup normal to see when going from debug to release (see also results on next slide)
Observation 3: Amount of time to get the result quite different
  Release mode build: the undesirable solution for 3D matrix is 30 times slower
    This is the case you see in practice – you build in release

## Slide 33: Observations on “Observation 1”
The fact that the results are the same is remarkable
Why remarkable?
  Finite precision arithmetic: addition loses its commutative and associative attributes
Because of finite precision
Because of finite precision

## Slide 34: Observations on “Observation 3” (most important)
First time in 759 discussing how to improve performance
  This type of gain; i.e., 30X speed up, not encountered every day…
Q: What mechanism comes into play to yield a 30X speed gain?
A: The cache
  L1 cache: 4 cycles
  System memory access: 120 cycles

## Slide 35: Indirection and how it’s hurting… An example. [one slide side trip]
Indirection: given an index i, you don’t need a[i]
  Rather, you need a[indir[i]] (this is one level of indirection; can go higher yet…)
What’s hurting here?
  First, when stride is large, you index into an array indir of non-negative integers but keep missing
    No locality…
  Second, you will subsequently jump in the array a all over the place
    Very likely you’ll just keep missing
Unfortunately, indirection in computing really common
void loop(int* a, unsigned int* indir, int N, int stride)
{
int sum = 0;
for (int i = 0; i < N; i+=stride)
sum += a[indir[i]];
}

## Slide 36: The Lesson Learned
Fact: Wide gap between using data and moving data
  Using data: you do sin of that data, log, pow, add, subtract, etc. (processing the data)
  Moving data: getting your data from the system memory (64 GB/128/etc. GB that you have on your system)
Fact: The cache used to close the big speed gap
Trait of well-written programs: they manage to leverage data/instruction locality
  Locality is what allows caches to come into play
  Locality necessary, but not sufficient (more later, “false sharing”)

## Slide 37: Memory Speed: Widening of the Processor-DRAM Speed Gap
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fourth edition
Notes: QUESTION: we talk about memory wall as an impediment to continuing increase in sequential computing performance and we said that the problem is that memory cannot keep up feeding the raw number crunching capability of the CPU.
But then, how can parallel computing be the answer? How could memory serve now multiple “consumers” and yet overall performance increase?
To explain this, we note that memory performance is related to two key concepts:
latency
bandwidth

## Slide 38: [Back to caches: The inner workings of caches] General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
The Cache
The Main Memory
Main Memory: Larger, slower, cheaper memory
(shown here as partitioned into “blocks” that are
mapped into cache lines)
Data copied in block-sized transfer units. Each block (such as block 10, for instance) typically holds 64 bytes of data (called cache line).
Smaller, faster, more expensive
memory can store a subset of
the main memory blocks
4
4
4
10
10
10
Everything handled in hardware. Invisible to programmer
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 39: Cache Line (aka Cache Block)
When data is brought in cache because a piece of data is needed, the MMU brings more than just the needed piece of data
Why bring more data than what absolutely necessary?
  Reason 1: In anticipation – recall principle of spatial locality
    You’ll likely need data that is right next to data that you just called for
  Reason 2: Because penalty is not high for bringing more: wide buses, little extra cost in bringing more data than exactly what needed
    For instance, NVIDIA hardware has 32 lanes for bringing data; it’s not like if you bring a bit more you have to pay significantly more
“cache line” - the size of the chunk of data brought from main memory and deposited into cache
  Many systems have cache line of 64 Bytes (8 doubles OR 16 floats OR 16 ints OR 64 chars, etc.)
  Cache line size is typically the same for L1, L2 and L3 caches

## Slide 40: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Delivery to registers…
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
Hit Rate: on average, how many out of 100 mem requests hit the cache?

## Slide 41: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where Block b goes
Replacement policy: determines which block gets evicted (victim)
Delivery to registers…
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →

## Slide 42: Cache Miss Classification, by Request Type [1/2]
Another way to classify cache misses is by the type of request leading to miss
Cache misses, by request type:
  Cache read miss from an instruction cache
  A cache read miss from a data cache
  A cache write miss to a data cache

## Slide 43: Cache Miss Classification, by Request Type [2/2]
Cache read miss from an instruction cache:
  Generally causes the most delay, because the processor, or at least the thread of execution, has to wait (stall) until the instruction is fetched from main memory
A cache read miss from a data cache:
  Usually causes somewhat less delay
  OOOE: Instructions not dependent on the cache read (if any) can be issued and executed until the data is fetched from main memory and the stalled instructions can resume execution
  TLP: Another thread can be picked up for execution
A cache write miss to a data cache:
  Generally causes the least delay – the write can be queued and there are few limitations on the execution of subsequent instructions
  The processor can continue unless the queue is full and then it has to stall for the write buffer to partially drain

## Slide 44: Reasons for Cache Misses
Cold (compulsory) miss
  When happens: cache is empty (e.g., beginning of the program, time slicing while having multiple programs in flight)
Capacity miss
  When happens: Not enough space, working set is too large
    Example: the active part of main memory overwhelms in size what can be accommodated by the cache
      You are asking for more than what level can accommodate (fit)
Conflict miss
  When happens: Enough space, but you have bad luck (lots of “conflicts”, as dictated by placement/replacement policy in place)
  Fact: In the memory hierarchy, the cache blocks at level map into a small subset of block positions at level
    Example: block at level must be placed in block () at level
  Conflict misses occur when the level cache is large enough, but multiple data objects all map to the same block in the level cache.
    Example: Referencing in this order blocks 0, 8, 0, 8, 0, 8, ... would miss every time (since )

## Slide 45: Placement & Replacement Policies
The cache is small, while the memory that you try to cache in this cache is large
  The cache: prime real estate – when somebody comes in, somebody else has to be evicted
Caching: like bringing folks from a city to live in one apartment building next to some prime attraction
  “prime attraction”: the registers and the ALU/CU
placement policy: deciding in which “apartment in the building” to drop the cache line
Sometimes, there are several rooms in an apartment: which one do you assign to the new folks?
  “replacement policy” – if you have Option A and Option B, which one should you choose: A or B?
    You’ll kick out tenant from room A, or tenant from room B

## Slide 46: Placement Policies
Policies that are common:
  “When you bring a line of cache…”
    You are free to place wherever (fully associative cache)
    Based on the main memory address of the data, you can put it in one of 4 places (four rooms in an apartment)
      Or 2 places, 8 places, or k places (for k-way associative cache)
    You can only put it in one place (direct mapped cache)

## Slide 47: Placement Policies: further discussion
Fully associative
  Pros: you have full control which old cache line you want to kick out (you have a very flexible replacement policy)
  Cons:
    Higher overhead to find what you’re looking for (data can be anywhere in cache)
    Higher overhead to decide whom to evict (the “victim”)
Direct mapped
  Pros: very fast to find if in cache or not
  Cons: might have to evict a line cache that actually sees a lot of use (no freedom at all in replacement policy)
K-way associative
  Decent compromise; i.e., it yields a reasonably decent replacement policy – you have K options to choose from
  Intel and AMD chips: 2, 4, 8, 16-way associative
    Depends on cache level and which chip model

## Slide 48: [New Topic:] General Cache Organization [Symbols Used and Their Meaning]
B: Number of bytes in a cache line
  Typically, B is 64
E: The number of cache lines (“Elements”) that huddle together
  Such a huddle is called “a set of cache lines”
  Typically, E is 1, 2, 4, 8, or 16 (other values possible)
S: the number of “Sets” that make up the cache
: total cache size

## Slide 49: The BEST rule: The “folks in an apartment building” metaphor
Folks from a big city driven to an apartment building to be in the proximity of big event
  How many folks will fit in this building?
The total number T of folks in the building depends on
  How many apartments in the building (S)
  How many rooms in an apartment (E)
  How many folks in a room (B)
Total number of folks in the building:

## Slide 50: General Cache Organization (B, E, S)
E = 2e lines per set
S = 2s sets
a “cache Set”
a “cache Element” (it wraps inside a cache line; an element belongs to a set)
0
1
2
B-1
tag
v
B = 2b bytes of data per cache block (cache line)
Cache size:
B x E x S=T data bytes
valid bit
[Bryant and O‘Hallaron: CMU] →
How a “cache Element” is organized

## Slide 51: On finding if data from a memory address is in cache or not
The mission: Read into register a variable at a given memory address
The important question: Is the value stored at this address by any chance in cache?
To answer this question, the addressed is partitioned in three chunks
t bits
s bits
b bits
Memory address (either 32 or 64 bits)
tag
set
index
block
offset

## Slide 52: How a cache read takes place
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes – the cache block (the data)
t bits
s bits
b bits
Memory address (either 32 or 64 bits):
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any element in set has matching tag
Yes + line valid = hit
  Locate data starting at offset
[Bryant and O‘Hallaron: Computer Systems - A Programmer's Perspective 3rd edition] →
How the game is played:

## Slide 53: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes (instead of 64)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
[Bryant and O‘Hallaron: CMU] →

## Slide 54: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes (instead of 64)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag
[Bryant and O‘Hallaron: CMU] →

## Slide 55: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes (instead of 64)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) that you care about is here
block offset
If tag doesn’t match: old line is evicted and replaced
[Bryant and O‘Hallaron: CMU] →

## Slide 56: E-way Set Associative Cache (Here: E = 2)
E = 2: Two elements/lines per set
Assume: cache block size 8 bytes (instead of 64)
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
2 elements per set
S sets
[Bryant and O‘Hallaron: CMU] →

## Slide 57: E-way Set Associative Cache (Here: E = 2)
E = 2: Two elements/lines per set
Assume: cache block size 8 bytes (instead of 64)
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag
[Bryant and O‘Hallaron: CMU] →

## Slide 58: E-way Set Associative Cache (Here: E = 2)
E = 2: Two elements/lines per set
Assume: cache block size 8 bytes (instead of 64)
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
[Bryant and O‘Hallaron: CMU] →

## Slide 59: Why these acrobatics?
Trying to fit a lot of memory (system memory, GBs of it) into little memory (cache, MBs of it)
Common sense: you have to use tricks to accommodate stuff from a big pot into a small pot
This dilemma of storing a lot of information in a small space is pervasive
  Due to the memory hierarchy reality we are operating under
  Similar tricks for placing data in main memory relative to placing in secondary memory

## Slide 60: Going on a tangent: TLP vs ILP
Chip can do more than one instruction per cycle
  ILP flavor: if chip is superscalar
  TLP flavor: two threads/processes run at same time, say A and B
Cache implications: TLP not positioned well
  On each miss by B, the cache victimizes an approximation of the least-recently-used (LRU) cache block
    Most of B’s misses will victimize blocks last accessed by A rather than last accessed by itself
  Consequences:
    The L1 cache turns over sufficiently fast that you can approximately assume that B victimizes all of A’s blocks
    Whether the L2 is completely flushed depends on B’s rate of misses, the L2 size, and how long B runs
[Mark Hill]