## Slide 1: ME759 High Performance Computing for Applications in Engineering [Spring 2020]
Lecture 07
02/05/2019
Dan Negrut, 2020 ME759 UW-Madison

## Slide 2: Quote of the day
“The greatest creative challenge is the struggle to be the architect of your own life.”
-- Wade Davis, Professor of Anthropology, University of British Columbia [1953 - ]

## Slide 3: Before we get going…
Last time:
  The mechanics of a cache operation (r/w)
  The B E S T formula for cache size
  The memory mountain
Today
  The Virtual Memory
  The 3 walls to sequential computing
Other tidbits:
  Assigned reading (syllabus gets updated)
  Assignment due on Th at 9 pm
  Use Piazza to get things going (for you or others)
t bits
s bits
b bits
Memory address (either 32 or 64 bits)
tag
set
index
block
offset

## Slide 4: Motivating Questions/Issues [1/3]
Question 1: How come you might have only 512MB of main memory on your laptop yet you can C-malloc an array of 1 GB?
Notes: Also, how can two processes that know nothing about each other refer to and use seemingly the exact same memory location (say 0x001a3df2)?
Moreover, what (where) is memory location 0x001a3df2?

## Slide 5: Motivating Questions/Issues [2/3]
Question 2: How can 20+ processes seemingly run at the same time? How do they each know where they can read/write data from/to?
  Assume I have 1 GB of RAM, and programA allocates 2 GB of memory and programB allocates 2 GB of memory. How can they run at the same time?
  Does programA need to know what addresses in memory it can use for data so that it doesn’t step on the feet of programB (and perhaps programC, programD, etc.)?
Notes: Also, how can two processes that know nothing about each other refer to and use seemingly the exact same memory location (say 0x001a3df2)?
Moreover, what (where) is memory location 0x001a3df2?

## Slide 6: Motivating Questions/Issues [3/3]
Question 3: How can you compile a program on a Windows workstation with 16 GB of memory and run it later on a different laptop with 1 GB of memory; i.e., less memory?
  Are there any problems w/ addresses being referenced by the instructions?
Notes: Also, how can two processes that know nothing about each other refer to and use seemingly the exact same memory location (say 0x001a3df2)?
Moreover, what (where) is memory location 0x001a3df2?

## Slide 7: Preamble, Virtual Memory
When you compile a program there is no way to know where in the physical memory the code will get its data allocated
  There are other “tenants” that inhabit the physical memory & they are already there before you get there
Solution: the code compiled under assumption that resulting process has undisputed access to 4 GB of pristine memory (on 32 bit systems)
  The “pristine memory” is called the virtual memory space
Notes: hardware (MMU: memory management unit) converts virtual addresses into physical addresses
OS provides support for paging (conceptually using more memory than physically available)

## Slide 8: Virtual vs. Physical Memory
Virtual memory: a dally and quaint fictitious space of 232 addresses (on 32 bit architectures) in which a process sees its data being placed, the instructions stored, etc.
Physical memory: a busy place that hosts at the same time data and instructions associated with tens of applications running on the system
For the virtualphysical memory trick to work out it take the interplay between the compiler, the operating system (OS), and the execution model embraced by the processor

## Slide 9: Why do we like Virtual Memory?
The Virtual Memory paradigm allows:
  Running programs that require more memory than physically available
  Running multiple programs “simultaneously” (multi-tasking)
  Handling of memory fragmentation/segmentation insofar as the main memory is concerned
  Transparent and unitary handling of memory and secondary storage (hard disk / solid state disk)
What is the hardware component that manages the Virtual Memory show?
  The Memory Management Unit (MMU)
    MMU part of the chip these days (back in the day, it used to be an entity by itself, off chip)

## Slide 10: The Virtual Memory: the anatomy of a living thing [How perceived by compiler & runtime]
addresses (32 bit OS)
Notes: Ignore for the moment the messiness of the physical memory and concentrate on how the “pristine” layout of the virtual memory is seen by a process.
Each process partitions its virtual memory layout in several segments as shown here.

## Slide 11: Anatomy of the Stack
Function bar and associated stack frame
  Should the function bar be called, this is how the stack should be pushed
  A “pop” operation is the opposite, it shrinks the stack
This is where the top of the stack used to be before function bar was called
Notes: Reasons for the stack: you don’t know how many times a function is called. The function needs to place its data somewhere, right? It’s like a hidden malloc followed by a copying the arguments (a and b, above) in this memory, which will also be hit by t1, t2, etc.
The stack is a segment of fixed size that is managed in a LIFO manner (push and pop).
Order of variables in stack is decided by compiler. Typically arrays are stored contiguously.
Note: stack also stores value of return address (from subroutine). This is a back-door that can be used by malicious programs to hijack execution: bar() above could try to write to initials[1000] in the hope to overwrite a return address for a function higher up in the call stack.

## Slide 12: Virtual Memory: The Page Table
Virtual memory allows the processor to work in a virtual world in which each process, when run by the processor, seems to have exclusive access to a very large memory space (, addresses, that is)
This virtual world is connected back to, or mapped back into, the physical memory through a Page Table (PT)
  This is one level of indirection
Notes: Back to the MMU’s job: Translating between virtual addresses and physical addresses. This is done through a so-called Page Table
To see how the PT works, let’s first dissect a virtual memory address…

## Slide 13: Anatomy of a Virtual Memory Address
A virtual address split into two parts (another case of address splitting, like for caches, when we split 3 ways):
  The page number
  The offset
Example below assumes a 32-bit OS with virtual pages of bytes
[physical memory]
Notes: The virtual memory is split into pages.
The physical memory is split into frames.
This is for a 32-bit OS with virtual pages of 4096 bytes.
4096 = 2^12  need 12 bits to indicate the offset in the page.
(Note: unit of address resolution is 8 bits  a virtual page holds 4 KB)
The remaining 32-12 = 20 bits used to index into the Page Table to get the corresponding frame number (which is held in N bits)

## Slide 14: Anatomy of a Virtual Memory Address
A page of virtual memory corresponds to a frame of physical memory
The size of a page (or frame, for that matter) is typically 4096 bytes
  Compare to 64 bytes, the size of a cache block (line)
212=4096: 12 bits of the address are sufficient to relatively position each byte in a page
  Bits marked 0 through 11 on the previous slide

## Slide 15: The Translation Process
Example: imagine that your physical memory is 2 GB
The physical address has 31 bits: 231=2GB
Then the page table converts the bits 12 through 31 of the virtual address into bits 12 through 30 of the physical address
Notes: N depends on the amount of available RAM:
e.g. for 2GB of RAM, N=19. Because 2GB=2^31 bits and 31=12+19
since N max = 20  a 32-bit OS can reference 4GB of memory  a maximum of 1 million pages
each address requires 4bytes  the PT takes 4MB
each active application has its own PT  lots of memory just for the PTs

## Slide 16: Comments on the Page Table (PT): Preamble to TLB
Page table enables the translation of virtual addresses into physical addresses
Every single process executing on a processor and managed by the OS has its own page table
Page table is stored in main memory
  For a 32-bit operating system size of a page table can be up to 4 MB in size
    4 MB: 2^20 addresses, each requiring 4(?) bytes to encode
  Start address of the PT for a process is stored in a dedicated register (PTR)
    The job of the Operating System to take care of this
Notes: Recall:
N depends on the amount of available RAM:
e.g. for 2GB of RAM, N=19. Because 2GB=2^31 bits and 31=12+19
since N max = 20  a 32-bit OS can reference 4GB of memory  a maximum of 1 million pages
each address requires 4bytes  the PT takes 4MB
each active application has its own PT  lots of memory just for the PTs
NOTE: memory requirements for PT even slightly larger than that: there are additional bits associated with each entry, e.g.
valid bit indicating if the physical address is on secondary storage
use bit used in LRU eviction strategy

## Slide 17: The TLB [Translation Lookaside Buffer] [1/2]
If you go to Page Table in main memory for each address translation this would be very costly
  One trip to translate address, one trip to actually fetch the data
There is a “cache” for the address translation process: TLB
  Translation Lookaside Buffer: holds the translation of a small collection of virtual page numbers into frame IDs
Notes: On page fault, the OS does the following:
data requested is located in secondary storage
request made for an entire (“surrounding”) frame to be brought over in main memory
room is made for the new frame as a virtual page (this may require evicting an existing one; e.g. using a LRU strategy)
the new frame is loaded in the virtual page
the PT is updated to reflect the change
control returns to process which is instructed to retry the instruction that led to a page fault

## Slide 18: Illustration: The role of the TLB
A TLB is just another cache
  Implemented in hardware, on-chip
A TLB miss leads to substantial overhead in the translation of a virtual memory address
Notes: Without a TLB, the purpose of caches would be defeated: a trip to memory would be required just to interrogate the PT to figure out the actual physical address of the required information (instruction or data)
Typically, TLB has between 16 and 512 entries.
Its “cache line” is 2 PT rows.
Mapping is usually fully associative.
Hit time very short (1 cycle)
Miss penalty 10-100 cycles
Typical TLB miss rate: 0.01 – 0.1%

## Slide 19: The TLB [Translation Lookaside Buffer] [2/2]
The Good, the Bad and the Ugly [1966, Rated R, w/ Clint Eastwood, 97% Rotten Tomatoes]
  The Good: the TLB leads to a hit and allows for quick address translation
  The Bad: TLB doesn’t have the required information cached and a trip to main memory in order
  The Ugly: the value at address that was just translated is not in cache and trip to main memory in order
  The Really Ugly: the requested frame not in main memory and a trip to secondary memory in order
    Called “page fault,” you’re hitting significant latency at this point
    “memory thrashing”: repeatedly hitting page fault upon page fault, to the point where time wasted in handling page faults dominates all the rest
Purpose of this slide: understand what happens when you don’t hit caches and you need to figure out where your data is and then fetch it
Notes: On page fault, the OS does the following:
data requested is located in secondary storage
request made for an entire (“surrounding”) frame to be brought over in main memory
room is made for the new frame as a virtual page (this may require evicting an existing one; e.g. using a LRU strategy)
the new frame is loaded in the virtual page
the PT is updated to reflect the change
control returns to process which is instructed to retry the instruction that led to a page fault

## Slide 20: Quick side-trip, speed of memory
A couple of lectures back, we saw 5X to 30X speedup if we hit the cache (good locality)
  Scenario: cache miss, you go to main memory
When handling large data sets, if they don’t fit in main memory and spill into secondary memory, lack of locality can lead to 1000X slowdowns
  Scenario: main memory page fault (even worse if you start getting into memory thrashing)

## Slide 21: Memory Access: The Big Picture, Includes Cache
A simplified version of how a memory request is serviced:
Notes: Note that the virtual memory mechanism allows looking at main memory as a “cache” for secondary storage.
Memory block  memory frame
Cache line (64 bytes)  virtual memory page (4096 bytes)
Cache miss  page fault
Note: page fault much more costly (secondary storage is even “farther” from RAM than RAM is to CPU)

## Slide 22: Quiz: Chop time for Cache read Virtual or Physical address?
To do, for instance, a cache read, you chop the address in three parts
Based on the picture at the right, what gets chopped in three parts: an address in virtual memory or in physical memory?

## Slide 23: Quiz: How many PTs?
ILP: you have a superscalar chip and can execute two instructions per clock cycle
  How many PTs will come into play?
TLP: your chip has assets to support two processes
  How many PTs will come into play?

## Slide 24: Memory-related aspects: various other tidbits
Going on several tangents
  Virtual vs. Physical memories: how their size comes into play
  Pointers in gdb/Visual Studio: pointing into virtual or physical memory?
  Unit of address resolution
  32 to 64 bit transition
  Frame size

## Slide 25: Virtual vs. Physical memories: how their size comes into play
Assumption: in this discussion we’re dealing with a 32 bit operating system
  Simpler to talk about it, fewer bits/smaller memories to keep track of. Nothing changes for 64 bit OSs
Case 1: The physical memory smaller than virtual memory
Case 2: The physical memory larger than virtual memory

## Slide 26: Case 1: Assume 2GB MB of RAM (my slim laptop)
2 GB of RAM: 2X more addresses in virtual memory than you have in physical memory
Depending how much memory your program uses, multiple virtual pages are going to be mapped into the same physical frame
Consequence: in reality, each entry in the Page Table always has [at least] one additional bit
  clean/dirty bit – indicates that translation to frame should not proceed immediately

## Slide 27: The Clean/Dirty Bit & the concept of Page Fault
Bit is “clean”: two conditions need to happen for the bit to be clean
  The frame that the page gets translated into has been loaded in main memory (think onset of execution)
  Since last translation, that very frame has not been associated with other virtual page
Bit is “dirty”:
  We called this before “page fault”, costly scenario to handle
  The OS will look for the needed frame on disk (secondary memory)
    The way you can think about it: the RAM (main mem) is the cache of the hard-disk (secondary mem)
      If bit in Page Table is dirty, the translation refers to address in secondary memory, not in main memory

## Slide 28: Case 2: Assume 16 GB of RAM (beefy workstation)
GB: this is good for your code, the likelihood of a memory frame getting evicted is smaller
PT should be “wide” enough (have enough bits) to recreate addresses to 16 GB of information
  You need 22 bits for pages of 4096 bytes:
    4096: 12 bits
    16 GB: need 34 bits to store addresses
    34-12=22 bits needed in each entry of the translation table
  NOTE: You have the same number of entries in the PT; they’re just wider compared to Case 1.
Note: clean/dirty bit also present if you have lots of physical memory since other programs run on the machine can render the bit “dirty”
  Imagine you run your code and Matlab comes in and starts working on 3.4 GB of memory
    Some of your frames will likely get evicted to disk
      Recall the concept of memory hierarchy, when things don’t fit, they’re send down the memory hierarchy

## Slide 29: [Short Topic] gdb/VS Pointers: Pointing In Virtual or Physical Memory?
Q: Is 0x000000DD582FFA18 an address in the virtual mem. or in the physical mem.?
A: This is a virtual memory address
  You see physical addresses if you are Linus Torvalds and work on kernel development
Quick note: addresses are provided in hex representation
Fewer digits to look at (would you prefer to look at 64 binary digits?)
Easy to figure out – each byte filled w/ binary digits translates into two digits out of the 16 hex digits used for the address
[https://inst.eecs.berkeley.edu/~cs61c/sp14/disc/12/dis12Sol.pdf]

## Slide 30: [Short Topic] The Unit of Address Resolution
How many bits are available for data storage at each address?
Example:
  We have 232 addresses that we can access
  If each address points to a location that stores 8 bits (one byte) then we have 4 GB of addressable memory
  However, if each address refers to a location that stores 2 bytes, we have 8 GB of addressable memory
Intel and AMD CPUs: the unit of address resolution is 1 byte (8 bits)
Consequence: the Intel 32 bit processors “see” a virtual memory space that can be 4 GB big and can reference each byte therein

## Slide 31: [New Short Topic] The 32 to 64 bit migration (1/2)
If the architecture and OS have 32 bits to represent addresses, it means that 232 addresses can be referenced
The data sets that we’re working with today are really large
  Having only 232 addresses to work with hardly enough
  Example: I have 32 GB of RAM and need to work with 8 GB array. How do I reach the end of array? Addresses are not large enough…
This motivated push towards having addresses represented using 64 bits:
  Memory space that I can address balloons to 264 bytes

## Slide 32: The 32 to 64 Bit Migration (2/2)
Note that a 64 bit architecture typically calls for two things:
  From a hardware perspective: size of the registers, translation tables, tags in caches, etc. – they need to change
  From a software/OS perspective, the program “operates” in a huge virtual memory space
    The new number of addressable bytes: 18,446,744,073,709,551,615
    In reality, the virtual memory addresses are represented using only about 40 to 50 bits
Notes: But, a shift from 32-bit to 64-bit isn’t an automatic win
“Your pointers will get bigger; your alignment boundaries get bigger; your data is less dense; equivalent code is bigger. You will fit less useful information into one cache line, code and data, and you will therefore take more cache misses. Everything, but everything, will suffer. Your processor's cache did not get bigger. Even other programs on your system that have nothing to do with the code you’re running will suffer. And you didn’t need the extra memory anyway. So you got nothing. Yay for speed-brakes.”
Rico Mariani (Microsoft) on why Visual Studio is still a 32-bit application

## Slide 33: Example [using CAE’s tux-103]
processor : 0
vendor_id : GenuineIntel
cpu family : 6
model : 60
model name : Intel(R) Core(TM) i5-4570 CPU @ 3.20GHz
stepping : 3
microcode : 0x20
cpu MHz : 3197.500
cache size : 6144 KB
physical id : 0
siblings : 4
core id : 0
cpu cores : 4
apicid : 0
fpu : yes
fpu_exception : yes
cache_alignment : 64
address sizes : 39 bits physical, 48 bits virtual
>> less /proc/cpuinfo

## Slide 34: [New Short Topic] The size of the frame/page
Refresher: a memory page, or virtual page, is a fixed-length contiguous block of virtual memory, described by a single entry in the Page Table
The frame is the fysical (or physical) counterpart of a virtual page
Typically, size of page is 4 KB but can be of 1024 KB for certain applications
  Example: working with very large data sets (big data)

## Slide 35: The size of the frame/page
Large page size, pros
  Less TLB pressure
  Why?
    Fewer pages to blanket the virtual memory means fewer entries in the Page Table, which means
      Fewer values that compete for storage in the TLB cache. More TLB hits: faster program
      [not that big of a deal] The size of the Page Table is smaller – less memory needed to store it
Large page size, cons
  Might lead to wasteful use of physical memory
    Example: page size 1024 KB. If you need to allocate 1030 KB of memory, you use two pages/frames
      If your process doesn’t use rest of the second page, then there’ll be a sizeable hole in physical memory

## Slide 36: The size of page/frame
[https://en.wikipedia.org/wiki/Page_(computer_memory)]
Architecture | Smallest page size | Larger page sizes
x86-64 | 4 KiB | 2 MiB, 1 GiB
UltraSPARC Architecture 2007 | 8 KiB | 64 KiB, 512 KiB, 4 MiB, 32 MiB, 256 MiB, 2 GiB, 16 GiB
SPARC v8 with SPARC Reference MMU | 4 KiB | 256 KiB, 16 MiB
Power Architecture | 4 KiB | 64 KiB, 16 MiB, 16 GiB
IA-64 (Itanium) | 4 KiB | 8 KiB, 64 KiB, 256 KiB, 1 MiB, 4 MiB, 16 MiB, 256 MiB
ARMv7 | 4 KiB | 64 KiB, 1 MiB, 16 MiB
32-bit x86 | 4 KiB | 2 MiB, 4 MiB

## Slide 37: Departing thoughts, memory aspects
Memory transactions:
  Add overhead, at times rather large, owing to complex process of moving data
    From disk to main memory to cache to register
  Time and power costly
Keep in mind the memory hierarchy; understand the size of the memories on your machine
  The closer to the top of the hierarchy, the better off you are
If the speed of the code matters, pay attention to how you use memory

## Slide 38: Side-trip: Using C/C++ in this class
Using C/C++ in this class: good vehicle to explain how memory works
  Two aspects that bring C close to hardware: pointers & the malloc (memory allocation) function call
The overhead of memory transactions is there in any language (Fortran, Matlab, Python, etc.)
For your favorite language, learn how indexing into your arrays doesn’t violate locality

## Slide 39: Parallel computing: why, and why now?

## Slide 40: Acknowledgements
Sources for some of the material presented today
  Hennessy and Patterson (Computer Architecture, 5th edition)
  John Owens, UC-Davis
  Darío Suárez, Universidad de Zaragoza
  John Cavazos, University of Delaware
  Others, as indicated on various slides
  I apologize if I included a slide and didn’t give credit where was due
  Any mistakes in these slides belong to me, not the individuals above

## Slide 41: Argument made in this segment of the course
Sequential computing execution speed pretty much flat for a decade now
Parallel computing is where speed improvements have come from

## Slide 42: Main causes for sequential computing speed stalling
Memory Wall
Instruction Level Parallelism (ILP) Wall
Power Wall
Not necessarily walls, but increasingly steep hills to climb
Source: “The Many-Core Inflection Point for Mass Market Computer Systems”, by John L. Manferdelli, Microsoft Corporation
    http://www.ctwatch.org/quarterly/articles/2007/02/the-many-core-inflection-point-for-mass-market-computer-systems/
Notes: Predicted in 2000:

## Slide 43: Memory Wall
Memory Wall: What is it?
  The growing disparity of speed between CPU and memory outside the chip
Memory accesses have gradually become a mighty barrier to computer performance improvements
  The trend: ever growing caches to improve average memory reference time to fetch or write instructions or data
    Caches are a transistor black hole
    Also, as cache gets gradually larger, it also gets gradually slower
Memory Wall: due to latency and limited communication bandwidth beyond chip boundaries.

## Slide 44: Memory Latencies [typical server and mobile computers]
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition
Server
Mobile
CPU
Registers
Notes: Hammad: in the fifth edition of the book embedded/mobile have their own diagram

## Slide 45: Memory Speed: Widening of the Processor-DRAM Performance Gap
Plot:*log* scale, the increasing gap between CPU and memory
  The memory baseline: 64 KB DRAM in 1980
Memory speed increasing rate: 1.07/year
Processors improved
  1.25/year (1980-1986)
  1.52/year (1986-2004)
  1.20/year (2004-2010)
You have the chops to process data, but can’t bring data to processor fast enough

## Slide 46: Memory Latency vs. Memory Bandwidth
Latency: the amount of time it takes for an operation to complete
  Measured in seconds
  The utility “ping” in Linux measures the latency of a network
  For memory transactions: send 32 bits to destination and back, measure how much time it takes gives you latency
Bandwidth: how much data can be transferred per second
  You can talk about bandwidth for memory but also for a network (Ethernet, Infiniband, modem, DSL, etc.)
Improving Latency and Bandwidth
  The job of folks in Electrical Engineering
  Once in a while, Materials Science colleagues deliver a breakthrough
  Promising technology: optic networks; layered memory on top of chip; etc.

## Slide 47: Memory Latency vs. Memory Bandwidth
Memory Access Latency more challenging to improve as opposed to improving Memory Bandwidth
Improving Bandwidth: add more “pipes”
  Requires more pins that come out of the chip for DRAM, for instance
  Adding more pins is not simple – very crowded real estate plus the technology is tricky
Improving Latency: no easy answer here
Analogy:
  If you carry commuters with a train, add more cars to a train to increase bandwidth
  Improving latency requires the construction of high speed trains (expensive/complex)

## Slide 48: Latency vs. Bandwidth: Recent Evolution of Speed Gains
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition
Notes: For the Microprocessor this is measured in MIPS (million instructions per second). Many reported IPS values have represented "peak" execution rates on artificial instruction sequences with few branches, whereas realistic workloads typically lead to significantly lower IPS values.

## Slide 49: Memory Wall, Conclusions [IMPORTANT SLIDE]
Take-home message: Long and winding conversations with main memory kills execution speed
Often times when you run your application, you are in one or both of these situations:
  You are far away from reaching top speed of the chip
  You may or may not be at top speed for your memory
    You are at top speed: you move lots of data, hitting the max bandwidth (ok, fact of life)
    You are not at top speed: you keep nibbling a little bit here and a little bit there – many trips all over the memory for small amounts of data
      Examples – sparse matrix operations, combinatorics, etc.

## Slide 50: Memory Wall, Conclusions [IMPORTANT SLIDE]
This is an important picture to have in mind when writing software
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition

## Slide 51: Another wall: Instruction Level Parallelism (ILP)
Instruction pipelining: the execution of multiple instructions overlapped; each instructions is divided into series of sub-steps (termed: micro-operations)
Superscalar execution: multiple execution units are used to execute multiple instructions in parallel
Out-of-order execution: instructions execute in any order but without violating data dependencies
Register renaming: a technique used to avoid data hazards and thus lead to unnecessary serialization of program instructions
Speculative execution: allows the execution of complete instructions or parts of instructions before being sure whether this execution is required
Branch prediction: used to avoid delays (termed: stalls). Used in combination with speculative execution.

## Slide 52: Intel Haswell example: ILP elicits very complex microarchitecture
[http://www.realworldtech.com/haswell-cpu/ ]
Notes: Dan - AGU: Address generation unit

## Slide 53: Sample Pipeline Depths
Pipeline Depth | Processors
6 | UltraSPARC T1
7 | PowerPC G4e
8 | UltraSPARC T2/T3, Cortex-A9
10 | Athlon, Scorpion
11 | Krait
12 | Pentium Pro/II/III, Athlon 64/Phenom, Apple A6
13 | Denver
14 | UltraSPARC III/IV, Core 2, Apple A7/A8
14/19 | Core i*2/i*3 Sandy/Ivy Bridge, Core i*4/i*5 Haswell/Broadwell
15 | Cortex-A15/A57
16 | PowerPC G5, Core i*1 Nehalem
18 | Bulldozer/Piledriver, Steamroller
20 | Pentium 4
31 | Pentium 4E Prescott
[http://www.lighterra.com/papers/modernmicroprocessors/]→

## Slide 54: The ILP Wall
Dedicated hardware speculatively executes future instructions before the results of current instructions are known, while providing hardware safeguards to prevent the errors that might be caused by out of order execution
Branches must be “guessed” to decide what instructions to execute simultaneously
  If you guessed wrong, you throw away that part of the result
Data dependencies may prevent successive instructions from executing in parallel, even if there are no branches
Predicting the future comes at the cost of microarchitecture complexity and power cost

## Slide 55: The ugly head of speculative execution
Speculative execution difficult to implement safely
Has become infamous for a recently-revealed series of bugs
  Meltdown (Intel, IBM, some ARM)
  Foreshadow (Intel)
  Spectre (everything before 2019 that uses branch prediction)

## Slide 56: [The last wall] The Power Wall
Power dissipation related to the clock frequency and feature length
  Consequence (the wall): clock rates are limited to some threshold value
Significant increase in clock speed without heroic/expensive cooling not possible. Chips would simply melt
Clock speed increased by a factor of 4,000 in less than two decades
  The ability of manufacturers to dissipate heat is limited though…
  Look back at the last ten years, the clock rates are pretty much flat

## Slide 57: The Power Wall
“Power, and not manufacturing, limits traditional general purpose microarchitecture improvements” (F. Pollack, Intel Fellow)
Leakage power dissipation gets worse as gates get smaller, because gate dielectric thicknesses decrease proportionately

## Slide 58: Dennard’s Scaling: Making Moore’s Law Useful
Dennard scaling: dictates how the voltage/current, frequency should change in response to smaller feature size
Voltage lower and lower, static power losses more prevalent
Transistors are too close
  We have many of them per unit area
Amount of power dissipated grows to high levels
  Thermal runaway
  Moving towards threshold at which computing not reliable
    What’s noise and what’s information?

## Slide 59: The “dark silicon”
Dark Silicon: transistors that manufacturers cannot afford to turn on
Too many transistors on a chip – cannot afford to power them lest the chip melts
Esmaeilzadeh, H.; Blem, E.; St.Amant, R.; Sankaralingam, K.; Burger, D., "Dark silicon and the end of multicore scaling," in Comp. Architecture (ISCA), 2011 38th Annual International Symp., pp.365-376, 2011

## Slide 60: One slide detour: “spending energy” rates
NVIDIA Tesla K80
  TDP: 300 Watts
Intel® Xeon® Processor E7-8890 v3
  TDP: 165 Watts
Human Brain
  20 Watts
  Represents 2% of our mass
  Burns 20% of all energy in the body at rest
  Our entire body, ball park: 100-120 Watts
Notes: [DN]
For a Opteron 6276, TDP is 115 W.
The Thermal Design Power (TDP) is the average maximum power a processor can dissipate while running commercially available software. TDP is primarily used as a guideline for manufacturers of thermal solutions (heatsinks/fans, etc) which tells them how much heat their solution should dissipate. TDP is not the maximum power the CPU may generate - there may be periods of time when the CPU dissipates more power than designed, in which case either the CPU temperature will rise closer to the maximum, or special CPU circuitry will activate and add idle cycles or reduce CPU frequency with the intent of reducing the amount of generated power.
TDP is usually 20% - 30% lower than the CPU maximum power dissipation.

## Slide 61: Shift in Perception
Increasing clock frequency is primary method of performance improvement
Processors parallelism is primary method of performance improvement
Less than linear scaling for a multiprocessor is failure
Even sub-linear speedups are beneficial as long as you beat the sequential on a watt-to-watt basis
Yesterday’s school of thought
Yesterday’s school of thought
Today’s take
Today’s take

## Slide 62: Conventional Wisdom in Computer Architecture
Old: Transistors expensive, Power is free
New: Transistors free, Power management very tricky (lots of power means heat to be dissipated and short battery lifespan)
Old: Multiplies are slow, Memory access is fast
New: Multiplies fast, Memory slow (200 cycles for DRAM memory access, 1 cycle for pipelined FMA)
Old : Increasing Instruction Level Parallelism hardware and compilers (Out-of-order, speculation, VLIW, …)
New: diminishing returns on more ILP
Power Wall
Memory Wall
ILP Wall
Notes: Power wall + Memory wall + ILP wall  BRICK wall

## Slide 63
Just a bunch of bad news…
OK, now what?

## Slide 64: The bright spot
We can produce small[er] transistors and we are increasingly good at packaging them in ICs

## Slide 65: Good news: number of transistors going up

## Slide 66: Moore’s Law (1965)
“The complexity for minimum component costs has increased at a rate of roughly a factor of two per year [see graph on next page]. Certainly over the short term this rate can be expected to continue, if not to increase. Over the longer term, the rate of increase is a bit more uncertain, although there is no reason to believe it will not remain nearly constant for at least 10 years. That means by 1975, the number of components per integrated circuit for minimum cost will be 65,000. I believe that such a large circuit can be built on a single wafer.”
“Cramming more components onto integrated circuits” by Gordon E. Moore, Electronics, Volume 38, Number 8, April 19, 1965

## Slide 67: Moore’s Law
1965 paper: Doubling of the number of transistors on integrated circuits every two years
  Moore himself wrote only about the density of components (or transistors) at minimum cost
http://news.cnet.com/Images-Moores-Law-turns-40/2009-1041_3-5649019.html

## Slide 69: Transistors bonanza: bringing happiness in lots of corners
Ability to cram more transistors per unit area and still make a profit good in many respects
  Microprocessors
  Storage controllers
  Memory capacity & speed

## Slide 70: 3D Stacked Memory
1st Generation (HBM1) introduced in AMD Fiji GPUs
  1GB & 128GB/s per stack
  AMD Radeon R9 Fury X: had four stacks  4GB & 512GB/s
2nd Generation (HBM2) used in NVIDIA Pascal/Volta and AMD Arctic Island GPUs
  2 GB & 256GB/s bandwidth per stack
  NVIDIA Volta approximately 900 GB/s memory bandwidth
  Apparently AMD has 1024 GB/s HBM available
SK Hynix’s High Bandwidth Memory (HBM)
  Developed by AMD and SK Hynix
Notes: PHY: die-to-die [physical?] interconnect (see https://www.synopsys.com/dw/ipdir.php?ds=dwc_die-to-die_phy)

## Slide 71: 3D Stacked Memory
Major step forward in performance.
Traditional GPU chip GDDR5 memory layout
New GPU (Pascal/Volta) chip HBM2 memory layout

## Slide 72: 3D Stacked Memory

## Slide 73: 3D Stacked Memory
Shorter distances
  Smaller latency nice!
  Less power required to move data
Smaller memory footprint
  16X smaller footprint
One HBM stack, made up of four DRAM dies (4-Hi)
Logic die

## Slide 74: Other Tidbits, HBM
HBM can stack up to eight DRAM dies, including an optional base die with a memory controller, which are interconnected by through-silicon vias (TSV) and microbumps.
HBM memory bus is very wide in comparison to other DRAM memories such as DDR4 or GDDR5.
Example:
  An HBM stack of four DRAM dies (4-Hi) has two 128-bit channels per die for a total of eight channels
    Width: 4 2 128 = 1024 bit wide per HBM stack
    GPU has four HBM stacks 4096 bit wide bus
  Bus width of GDDR memories is 32 bits per channel, with 16 memory chips for a graphics card with a 512-bit memory interface.
NOTE: HBM supports now up to 4GB per stack
  Pascal GPU: There are four stacks 16 GB
  Intel Xeon Phi Knight Landing: MCDRAM, 16 GB [retired by Intel, deadend]
Notes: [Colin] NVIDIA has been moving to GDDR6 due to performance-limiting heat dissipation problems with stacked memory
[Colin] Cost of HBM manufacturing very high

## Slide 75: Moving to the processor: transistor counts per microprocessor

## Slide 76: Intel Roadmap [or other folks’ roadmap]
2013 – 22 nm Tick: Ivy Bridge – Tock: Haswell
2015 – 14 nm Tick: Broadwell – Tock: Skylake
2016 – 14nm “Refresh” Kaby Lake
2017 – 10 nm Cannon Lake (delayed to 2019)
2019 – 7 nm [Radeon Instinct MI60 (no Intel here)/Zen2]
2021 – 5 nm
2023 – 3 nm (? Samsung)
Notes: Hammad: Even intel is having problems going down in process technologies. 10nm was delayed until the second half of 2017. Broadwell didn’t have good yields, they never released a desktop version (only laptop) and went straight to skylake for desktop CPUs

## Slide 77: Parallel computing: The Ox vs. Chickens Analogy
Ox: one powerful CPU core, running at high frequency, lots of cache to hide memory latency
Chicken: many meagre processors, running at lower frequency, not much cache or brain (like in CU)
  Requires other ways to hide memory latency
Few were eating chicken a decade ago but popular now
“If you were plowing a field, which would you rather use: Two strong oxen or 1024 chickens?” [Seymour Cray]

## Slide 78: Two examples of Parallel HW: Putting to good use billions of transistors
Intel Haswell
  Multicore architecture
  Four oxen, that is
NVIDIA Fermi
  Large number of scalar processors (“shaders”)
  512 chicken, that is

## Slide 79: Intel Haswell
June 2013
22 nm technology
1.4 billion transistors
4 cores, HTT
Integrated GPU
System-on-a-chip (SoC) design
Notes: Direct Media Interface (DMI) is the link between the northbridge and southbridge on a computer motherboard

## Slide 80: Haswell example: multi-core architecture (four oxen)
Shared-Memory Multiprocessor Architecture
Courtesy of Elsevier, Computer Architecture, Hennessey and Patterson, fifth edition
SRAM
DRAM
SRAM
Notes: Hammad – Updated Figure from fifth edition

## Slide 81: The Fermi Architecture [ Schematic of a NVIDIA Stream Multiprocessor (SM)]
Late 2009, early 2010
40 nm technology
Three billion transistors
512 Scalar Processors (SPs), or “shaders”
  This is the chicken
L1 cache
L2 cache
6 GB of global memory
Operates at low clock rate
High bandwidth (close to 200 GB/s)

## Slide 82: A Fermi SM (Streaming Multiprocessor; one of 16)
Not a whole lot of brain here, yet a lot of power

## Slide 83: Fermi: 30,000 feet perspective, the entire chip
Lots of ALU (green), not much of CU (orange)
Explains why GPUs are fast for high arithmetic intensity applications
Arithmetic intensity: high when many operations performed per byte of data

## Slide 84: The CPU and GPU: their true colors
The GPU is specialized for compute-intensive, highly data parallel computation (owing to its graphics rendering origin)
  More transistors devoted to data processing rather than data caching and control flow
  Where are GPUs good: high arithmetic intensity (the ratio between arithmetic operations and memory operations)
The video game industry exerts strong economic pressure that pushes things forward in GPU computing
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU

## Slide 85: Beefy CPU vs. beefy GPU comparison, 2019
 | GPU – NVIDIA Tesla V100 32GB $8,995 | CPU – Intel® Xeon® Platinum 8180 $10,009
Processing Cores | 5120 CUDA Cores 640 Tensor Cores | 28 cores (56 threads, SMT)
Memory | 32GB HBM2 | - 64 KB L1 (I+D) cache / core - 1 MB L2 cache / core - 38.5 MB L3 cache (1.375 MB / core), average
Clock speed | 1.29 GHz | 2.5 GHz (3.80 GHz Turbo; Throttles to 2.3 GHz when all FP units are active)
Memory bandwidth | 900 GB/s | 119.21 GB/s (19.87 GB / channel / s)
Floating Point Throughput | 7.8 Double Precision TFLOP/s 15.6 Single Precision TFLOP/s | 2.0608 Double Precision TFLOP/s
TDP | 300 Watts | 205 Watts
https://en.wikipedia.org/wiki/Nvidia_Tesla
https://www.techpowerup.com/gpu-specs/tesla-v100-sxm2-32-gb.c3185
https://en.wikichip.org/wiki/intel/xeon_platinum/8180
https://ark.intel.com/products/120496/Intel-Xeon-Platinum-8180-Processor-38-5M-Cache-2-50-GHz-

## Slide 86: [side trip, 1/2] on-chip vs. on-package vs. off-package
Where a resource is dictates to a large extent its communication latency and/or bandwidth
Example, on-chip: Intel Haswell has the GPU on the same chip with the rest of the CPU
Example, on-package: the 128 MB of eDRAM available on Intel Core i7 4950HQ
The GPU is on-chip
The eDRAM is on-package

## Slide 87: [side trip, 2/2] on-chip vs. on-package vs. off-package
Example, off-package vs. on-package: traditional memory vs. HBM
Off-package Example chip GDDR6 memory
On-package Example chip HBM2 memory